Petition No. 446

AT&T Wireless PCS, Inc.

Staff Report

April 12, 2000

On March 8, 2000, Connecticut Siting Council (Council) member Gerald J. Heffernan, and Fred Cunliffe of Council staff met AT&T Wireless PCS (AT&T) representatives Michael Murphy and Daniel Garber and Michael Austin of Pinnacle Site Development for inspection of a Connecticut Light & Power Company (CL&P) electric transmission line structure (no. 1102) located off Willruss Court in Norwalk.  AT&T, with the agreement of CL&P, proposes to modify the transmission structure for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

AT&T proposes to attach an 8.6-inch diameter pipe extending the existing structure height of 94 feet by 12 feet for a total height of 106 feet.  AT&T proposes a low profile antenna cluster mount at the top of the pipe and placing associated equipment cabinets on a steel frame within the base of the existing structure. The proposed site is on property owned by CL&P within an urban setting consisting primarily of residential homes.  Eight residences are within approximately 200 feet of the proposed site. Buffers of vegetation exist on both sides of the right-of-way.

Minor clearing of vegetation and debris is expected both for the site and to improve an existing access from Willruss Court to the structure. A 30 ft. by 40 ft., 8-foot high chain link fence would surround the structure. Utilities would be routed underground within the access drive approximately 100 feet from an existing utility pole to the site.

The worst case power density for the telecommunications operations at the site has been calculated to be less than 2.6% of the applicable standard for uncontrolled environments.  AT&T contends that the proposed installation will not cause a substantial adverse environmental effect, and for this reason would not require a Certificate.