Petition No. 455

AT&T Wireless PCS, Inc.

Wilton, Connecticut

Staff Report

May 10, 2000

On May 8, 2000, Connecticut Siting Council (Council) member Edward S. Wilensky, and Fred Cunliffe of Council staff met AT&T Wireless PCS (AT&T) representative Michael Austin of Pinnacle Site Development for inspection of a Connecticut Light & Power Company (CL&P) electric transmission line structure (no. 2998) located at 289 Danbury Road (Route 7) Wilton.  AT&T, with the agreement of CL&P, proposes to modify the transmission structure for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

AT&T proposes to attach an 8.6-inch diameter pipe extending the existing structure height of 96 feet by 5 feet for a total height of 101 feet.   A structural analysis concludes no additional reinforcement is necessary for this proposal.  AT&T proposes a low profile antenna cluster mount at the top of the pipe.  Also, AT&T would place associated equipment cabinets on a steel frame on concrete piers adjacent to the base of the existing structure within CL&P’s right-of-way.  The proposed site is adjacent to the Wilton Railroad Station and hidden behind commercial businesses on Route 7.  Staff believes no landscaping would be needed.

An existing paved access from Danbury Road would be used by AT&T to access the structure.  A 20-foot by 23-foot, 8-foot high chain link fence would surround the equipment and structure.  Utilities would be routed underground within the access drive approximately 200 feet from an existing utility pole to the site.

The worst case power density for the telecommunications operations at the site has been calculated to be less than 3.4% of the applicable standard for uncontrolled environments.

AT&T contends that the proposed installation will not cause a substantial adverse environmental effect, and for this reason would not require a Certificate.