Petition No. 457

Voicestream Wireless

Bethel, Connecticut

Staff Report

May 10, 2000

On May 4, 2000, Connecticut Siting Council (Council) member Gerald J. Heffernan, and Fred Cunliffe of Council staff met Voicestream Wireless (Voicestream) representatives J. Brendan Sharkey, Esq., Chetan Dharduk, and Brian Raggazine for inspection of a Connecticut Light & Power Company (CL&P) electric transmission line structure (no. 10256) located off Chimney Drive, Bethel.  Voicestream, with the agreement of CL&P, proposes to modify the transmission structure for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

Voicestream proposes to attach a 4.5-inch diameter pipe extending the existing monopole height of 150 feet by 25 feet 4 inches for a total height of 175 feet 4 inches.  A structural analysis concludes no additional reinforcement is necessary.  No microwave antenna is proposed as depicted in the antenna drawing. Voicestream proposes to install two low profile antenna cluster mounts with centers of radiation at 173 feet and 163 feet 4 inches on the pipe, and place associated equipment cabinets on a concrete foundation within a 10-foot by 20-foot compound secured by a six-foot chain link fence.  Utilities would be placed underground 150 feet from an existing electric transformer and telephone junction box to the site.  No trees would be cleared to install the utilities.

The proposed site is within a CL&P easement within a residential area. The nearest home is across Chimney Drive approximately 200 feet west of the site with other homes nearby.  The same trees not to be cleared for installation of utilities would provide a buffer to these homes.

The worst case power density for the telecommunications operations at the site has been calculated to be less than 3.6% of the applicable standard for uncontrolled environments.

Voicestream contends that the proposed installation will not cause a substantial adverse environmental effect, and for this reason would not require a Certificate.