Petition 462

Remote Meter Reading Project - Cell Master Units

The United Illuminating Company

Staff Report

May 24, 2000

On May 22, 2000, Connecticut Siting Council (Council) member Gerald J. Heffernan and Council staff Paul M. Aresta met United Illuminating Company (UI) representatives Kathleen Shanley and Peter C. Costabile for a field a review of this petition.  UI is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need would be required for the placement of an antenna and associated equipment as part of a remote meter reading network at Canisius Hall, Fairfield University, Fairfield, Connecticut.

UI proposes to install a Cell Master Unit (CMU), consisting of an approximately ten-foot high by three-inch diameter antenna and a base station equipment cabinet.  The proposed antenna would be mounted at approximately the 28-foot level of an existing 33-foot self-supporting lattice tower atop the roof of a 55-foot building.  The proposed base station equipment cabinet would be approximately 49 inches high by 44 inches wide by 20 inches deep and would be mounted directly to the penthouse wall, approximately two feet above the roof.

The proposed CMU would serve as a regional data collector for receiving transmitted metering information from micro cell controllers (MCCs), and then forward the metering data via land line to UI’s corporate headquarters.  The proposed CMU would transmit a signal to the MCCs it serves while operating at a maximum of five watts on one channel at a height approximately 88 feet above ground level for a predicted maximum electromagnetic power density of 0.036 percent of the applicable ANSI standard for the general population.

UI contends that the proposed project would not impact wetlands nor would any vegetation be removed; and that the use of an existing telecommunications site minimizes the visual impact and any potential adverse environmental effects.