Petition No. 480

Connecticut Light and Power Company

Middletown, Connecticut

Staff Report

September 19, 2000

On September 14, 2000, Connecticut Siting Council (Council) member Mortimer A. Gelston and staff members Christina Lepage and Fred Cunliffe met Robert Charpentier of Connecticut Light and Power Company (CL&P) for inspection of a CL&P substation located on South Main Street (Rt. 17), Middletown.  CL&P proposes to modify the Dooley Substation and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

CL&P proposes the installation of one 115- to 13.2-kV power transformer with associated equipment, and one 13.2-kV voltage regulator within an existing fence line.  Sumps would be placed under the both pieces of the proposed equipment as a precaution in the case of an oil spill.  The existing site currently contains one power transformer with an internal voltage regulator, the failure of which will cause a blackout in the area.  The substation serves local distribution feeders from two 115-kV transmission lines.  The proposed equipment will be used as a back up in the case of a failure of the existing power transformer.

The proposed site is within the existing CL&P Dooley Substation fenced area located on South Main Street (Route 17), Middletown, CT.  An existing access road will continue to be used to access the site.  The existing substation is located within an area zoned residential with the closest residential dwelling approximately 500 feet to the north of the site.  Wetlands and waterways do not exist on the property; the closest wetland is approximately fifty feet to the west of the substation.

CL&P contends that the installation of the proposed structures would have no visual impact to the surrounding area; noise levels at the property lines would remain below state limits; there would be no interference to television or radio; the project is not within a 100-year flood zone or stream channel encroachment lines; and the wetlands and waterways on the site would not be affected by this addition; therefore, there would be no substantial adverse environmental impact.