Petition No. 485

VoiceStream Wireless

New Milford, Connecticut

Staff Report

November 14, 2000

On September 29, 2000, Connecticut Siting Council (Council) member Edward S. Wilensky and Christina Lepage of the Council staff met with VoiceStream Wireless (VoiceStream) representative Brian Ragozzine on Route 202 near Russeling Ridge Road, New Milford, Connecticut for inspection of an electric transmission structure. The property and structure is owned by Connecticut Light and Power Co. (CL&P).  VoiceStream Wireless, with the agreement of CL&P, proposes to modify the structure by installing antennas and associated equipment for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

VoiceStream proposes the installation of four EMS dual pol antennas in a cluster mount attached vertically on top of a 3-inch pipe mast in two sectors with two antennas per sector.  The slender design of the pipe mast configuration blends with the underlying structure.  The antennas will extend approximately 17 feet 4 inches above the existing 68-foot guyed electric transmission structure (#2069).  The height at the top of the antennas will be 85 feet 4 inches above ground level (agl).  The centerline for the upper antennas will be 83 feet agl, and the centerline for the lower antennas will be at 76 feet 4 inches agl.  This design requires the spacing to be a minimum of six feet above the CL&P shield wire and two feet between the antennas.  The cables for the installation will be placed inside the leg of the existing structure.  A 3/8-inch diameter guy cable will be installed on the north side of the tower to augment an identical guy on the south side.

The Nortel S8000 equipment cabinet will be mounted on a 10’ x 11’ fenced concrete slab north of the existing tower.  VoiceStream believes that landscaping around the fenced compound might draw more attention to the facility because the existing tower is located in an open field.  However, VoiceStream is prepared to install landscaping on the site if the Council deems it necessary.  The equipment cabinet does not require any protective structures or air conditioning; therefore no audible noise will be created.  An underground conduit within the CL&P right-of-way will provide telephone service and power to the site.

The proposed site is located west of Route 202 in New Milford.  The zoning designation of this site is R-80 Residential District.  Land use in the surrounding area is primarily single-family residential and open space, with some businesses north and south along Route 202.  The closest residence is 500 feet to the north of the proposed site, however there are other residences along Route 202 that are a close proximity to and within the sight-line of the proposed structure.  Notification of the project has been delivered to the three abutting landowners.

VoiceStream contends that the increase in height of this monopole structure will not result in a substantial environmental effect.  The proposed project will prevent the construction of a new tower in the area.  VoiceStream also states that the PCS antennas will blend in with the existing transmission line structure and the placement of the associated equipment, which will be directly underneath the existing tower, will limit the disturbance created by construction activities.  When operations have stopped, VoiceStream will dismantle the equipment located at the site.  If the Council deems it necessary, VoiceStream is willing to post a bond with the Town of New Milford to cover the cost of removal of the equipment in the event that the site is abandoned.

The worst-case power density for the telecommunications operations at the site has been calculated to be 4.92% of the applicable standard for uncontrolled environments.  If the Council wishes, VoiceStream will perform field measurements of its actual power density during operations after the site is completed, and provide that information to the Council and the Town of New Milford.

This petition was tabled on October 2, 2000 to review comments from abutting landowners and to consider an alternative site location on an existing Springwich tower located approximately 1 mile South of the proposed site.  The Council has not received comments from neighbors.

VoiceStream submits that the proposed modification of the structure would not require a Certificate because it will reduce the need for a new telecommunications tower by utilizing an existing structure and contends that the proposed installation will not cause a substantial adverse environmental effect.