Petition No. 488

Connecticut Light and Power Company (CL&P)

Greenwich, Connecticut

Staff Report

November 2, 2000

On October 30, 2000, Connecticut Siting Council (Council) member Gerald J. Heffernan and Council staff Paul M. Aresta met CL&P representatives Christopher C. Swan and Arron L. Goucher for an inspection of the Cos Cob Substation located off Sound Shore Drive, in Greenwich.  CL&P is petitioning the Council for a declaratory ruling that the proposed upgrade of equipment at the existing Cos Cob Substation would not have a substantial adverse environmental effect.

CL&P proposes to install a new 25-MVA, 115 to 13.2-kV transformer and a power/control enclosure with a metalclad switchgear.  The proposed transformer would be approximately 27 feet long by 22 feet wide by 11 feet high, and the power/control enclosure would be approximately 22 feet long by 14 feet wide by 7.5 feet high.  The proposed equipment is required to increase capacity and improve reliability of the Cos Cob Substation.  The proposed transformer would be located approximately 110 feet east of the proposed metalclad switchgear; however, the proposed equipment would be located within the fenced compound of the existing electric generation and substation site.  An easement has been obtained from NRG for the underground connection of the proposed metalclad switchgear with the proposed transformer.

The proposed equipment would not be located within wetlands or waterways, the 100-year flood zone, or any channel encroachment lines.  CL&P contends that the proposed equipment upgrades would have no visual impact; would not exceed state sound level standards; would not cause interference for television or radio; and would not adversely affect the environment, or scenic, historic, and recreational resources.