Petition No. 495

Springwich Cellular Limited Partnership

Staff Report

December 14, 2000

On December 12, 2000, Connecticut Siting Council (Council) member Dr. William H. Smith and Christina Lepage of the Council staff met with Springwich Cellular Limited Partnership (SCLP) representative Peter van Wilgen at the Seton Boy Scout Reservation off of Riversville Road, Greenwich, Connecticut for a site inspection for the proposed replacement of an existing telecommunications tower and expansion of the site boundaries to accommodate tower sharing.  SCLP is petitioning the Council for a declaratory ruling that the proposed project would have no substantial adverse environmental effect.

SCLP proposes to replace an existing 150-foot monopole structure with a new 150-foot monopole structure and increase the site boundaries to accommodate tower sharing by SCLP, VoiceStream Wireless (VoiceStream), Verizon Wireless (Verizon), Nextel Communications (Nextel), AT&T Wireless (AT&T), and Sprint PCS (Sprint).  The existing tower, which was approved by the Council in Docket 50, measures approximately 3-feet at the base and 1-foot at the top. The existing tower is not capable of supporting the additional carriers’ antennas requiring the construction of a new tower of stronger design, measuring approximately 5.5 feet at the base and 2.5 feet at the top.

The replacement tower is proposed to be located approximately 100 feet southwest of the existing tower, and would support the antennas for SCLP at the 150-foot level; Verizon at the 140-foot level; Nextel at the 130-foot level; Sprint at the 120-foot level; AT&T at the 110-foot level.  In addition, VoiceStream would place an antenna array on a mounting post at the top of the replacement tower resulting in an overall height of approximately 163 feet including appurtenances.  The tower has been designed to allow at least one additional antenna platform at the 100-foot level.

The site currently occupies a 50’ x 50’ leased area consisting of the existing 150-foot monopole, a two-carrier equipment building, and other associated equipment enclosed within a fenced area.  Nextel and AT&T will be installing equipment rooms.  The existing 8-foot high chain-link fence would be extended around all of the equipment structures.  The access road will be extended about 90 feet within the fenced area.

The height of the tower will remain unchanged.  The noise levels at the existing facility would not increase by six decibels, under normal operating conditions. The operation of all the carriers’ proposed antennas would not exceed the maximum permissible exposure limit for the worst case radio frequency power density at the base of the structure.  The calculated cumulative worst case power density would not exceed 23.7% of the applicable standard.  Approximately one-tenth of an acre of trees will have to be removed to expand the site area.  Most of the trees within the area to be cleared are young, measuring one inch to six inches in diameter, with a few larger trees measuring up to 18 inches in diameter.  The trees to be cleared include maple, hickory, oak, fir, and tulip poplar.  SCLP contends that the incremental visual impact from placing additional antennas on one tower is preferable to the construction of multiple towers.

SCLP contends that the proposed replacement of an existing 150-foot tower and expansion of the site boundaries to accommodate tower sharing does not cause a significant change or alteration in the physical and environmental characteristics of the site, and would not cause a substantial adverse environmental effect.