Petition No. 506

VoiceStream Wireless

Waterford, Connecticut

Staff Report

April 26, 2001

On April 20, 2001, Connecticut Siting Council (Council) Chairman Mortimer A. Gelston and Christina Lepage of the Council staff met with VoiceStream Wireless (VoiceStream) representatives Kurt Sheathelm and Cindy Unsworth off of Oil Mill Road, Waterford, Connecticut for inspection of an electric transmission structure. The property and structure is owned by Connecticut Light and Power Co. (CL&P).  VoiceStream Wireless, with the agreement of CL&P, proposes to modify the structure by installing antennas and associated equipment for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

VoiceStream proposes the installation of three antennas on top of a 4.5-inch pipe mast extension.  The antennas will extend approximately 10-feet 7-inches above the existing 82-foot transmission line monopole structure (#6063).  The height at the top of the antennas will be 92-feet 7-inches above ground level (AGL), with a centerline of 90-feet AGL.  This design requires a minimum of six feet above the CL&P shield wire.

A Nortel S8000 equipment cabinet will be mounted on a 7’8” x 5’6” concrete slab within a 13’6”x11’7” fenced compound at the base of the tower.  The equipment cabinets do not require any protective structures or air conditioning; therefore no audible noise will be created.  An underground conduit from an adjacent utility pole will provide power and telephone service to the site.  A paved drive will be used to access the site.  An existing stone wall will be relocated and rebuilt along the access drive.

The proposed site is located east of the intersection of Interstates 95 and 395, and east of Oil Mill Road.  The zoning designation of this site is RU-120 (rural/residential).  VoiceStream identified the surrounding land use as primarily rural and residential; the nearest residence is approximately 350 to 400 feet to the north-northeast.  The nearest buildings are part of a farm, which is approximately 300-feet to the northeast of the site.

The worst-case power density for the telecommunications operations at the site has been calculated to be 1.9355% of the applicable standard for uncontrolled environments.

VoiceStream contends that the proposed modification of the structure would not require a Certificate because the increase in height of this monopole structure will not result in a substantial environmental effect and the proposed project will prevent the construction of a new tower in the area.  VoiceStream also states that the PCS antennas will blend in with the existing transmission line structure, and the placement of the equipment cabinets, which will be directly underneath the existing tower, will limit the disturbance created by construction activities.