Petition No. 529

AT&T Wireless PCS, LLC

Darien, Connecticut

Staff Report

November 7, 2001

On November 5, 2001, Connecticut Siting Council (Council) member Gerald J. Heffernan and Christina Lepage and Robert Mercier of the Council staff met with AT&T Wireless PCS, Inc. (AT&T) representative Peter Carbone off of Hollow Tree Ridge Road, Darien, Connecticut for inspection of an electric transmission structure. The property and structure is owned by Connecticut Light and Power Co. (CL&P).  AT&T, with the agreement of CL&P, proposes to modify the structure by installing antennas and associated equipment for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

AT&T proposes the installation of three panel antennas on a 6.6-inch diameter lattice extension.  The antennas would extend approximately 12-feet above the existing 90-foot transmission line lattice structure (# 1180).  The height at the top of the antennas would be about 102-feet above ground level (AGL), with a centerline of 100-feet AGL.

Equipment cabinets will be located on a 12-foot by 20-foot concrete pad within a 18-foot by 28-foot compound with an 8-foot high stockade fence adjacent to the base of the tower.  An underground conduit from an existing utility pole will provide power and telephone service to the site.

The proposed site is located at the Noroton Railroad Station.  The zoning designation of this site is Parking Residential (PR).  AT&T identified that the surrounding landscape is comprised of transmission towers, high voltage lines, right-of-way, the railroad station, Interstate 95 and commercial uses.

The worst-case power density for the telecommunications operations at the site has been calculated to be 3.17% of the applicable standard for uncontrolled environments.

AT&T contends that the proposed modification of the structure would not cause a substantial adverse environmental impact and would prevent the construction of a new tower in the area.  AT&T also states that the proposed facility would not be out of scale with the existing surrounding landscape.