Petition No. 534

Connecticut Light & Power Company

Card Substation

Lebanon, Connecticut

Staff Report

December 11, 2001

On December 3, 2001, the Connecticut Light & Power Company (CL&P) submitted to the Connecticut Siting Council (Council) a petition for a determination that no Certificate of Environmental Compatibility and Public Need would be required for proposed modifications to CL&P’s Card Substation because the proposed modifications would not have a substantial adverse environmental effect.

On December 6, 2001, Gerald Heffernan of the Council and Robert K. Erling of the Council staff met Kris Aberg of CL&P for a field review of the proposed construction at the Card Substation in Lebanon, Connecticut.  CL&P proposes to add one 115-kW to 23-kV MVA transformer and one 23-kV feeder position at the Card Substation.  This equipment would serve to improve system reliability and increase the 23-kV substation capacity.  Specifically, CL&P proposes to install one 115-kV disconnect switch, approximately 450 feet of underground 115-kV power cable; one 115- to 23-kV 47-MVA transformer; and one 23-kV transformer circuit breaker.  CL&P had originally planned to add two 115- to 23-kV transformers in the 1970’s, but due to slow load growth, only added one transformer.

The Card Substation is a large facility with sufficient room for the addition of equipment within its fenced boundaries.  The substation is surrounded by wooded parcels of land and there are few homes in the area.

CL&P proposes to begin construction in February 2002, with completion of the project expected by the end of May 2002.

Robert K. Erling

Senior Siting Analyst