Petition No. 537

Connecticut Light and Power Company (CL&P)

Stonington, Connecticut

Staff Report

January 3, 2002

On December 19, 2001, Connecticut Siting Council (Council) member Pamela B. Katz and Council staff Paul M. Aresta met CL&P representative Robert J. Charpentier for an inspection of the Mystic Substation located on Greenmanville Road (Route 27), in Stonington, Connecticut.  CL&P is petitioning the Council for a declaratory ruling that the proposed installation of approximately 400 feet of 115-kV solid dielectric cable, two 115-kV capacitor banks, and associated equipment at the existing Mystic Substation would not have a substantial adverse environmental effect.

CL&P proposes to install two 115-kV, 25.2-MVAR capacitor banks, a 115-kV circuit breaker, one set of 115-kV current limiting reactors, a 115-kV disconnect switch, two 115-kV circuit switches, and approximately 400 feet of 115-kV solid dielectric cable.  The proposed 115-kV solid dielectric cable would be installed below ground along the northern fence line between the capacitor banks and current limiting reactor.  The proposed equipment would be located within the existing fenced area, and would be no taller than approximately 22 feet high.  The proposed equipment is required to improve area transmission voltage levels during contingency conditions.  The proposed work would begin in January 2002, and be completed by the end of May 2002.

The proposed equipment would not be located within wetlands or waterways, the 100-year flood zone, or any stream encroachment lines.  No vegetation would be removed.  CL&P contends that the proposed equipment upgrades would have no visual impact; would not cause interference for television or radio; and would not adversely affect the environment, scenic, historic, and recreational values.