Petition No. 538

Crown Castle International

Suffield, Connecticut

Staff Report

January 17, 2002

On December 28, 2001, Connecticut Siting Council (Council) member Daniel P. Lynch and Fred Cunliffe of the Council staff met with Crown Castle International (Crown) representative Shane Newhart and Steven Levine of Cingular Wireless (Cingular) at 44 Fyler Road Suffield, Connecticut for inspection of an existing 95-foot monopole telecommunications tower. The site is located at the Town of Suffield Public Works garage. The Town approved this tower on May 1, 2000, and is owned by Crown.  Crown proposes to increase the height from 95 feet above ground level (AGL) to 110 feet AGL for the purposes of installing antennas owned by Cingular and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

Cingular proposes extending the height of the tower to 110 feet AGL, and installing twelve panel antennas on a triangular antenna platform. The height at the top of the antennas will be about 110 feet AGL with the antenna centerline at 107 feet AGL.  A 12-foot by 20-foot equipment shelter will be located near the base of the tower.

Verizon Wireless currently shares the tower at the 92-foot level, Nextel at the 82-foot level, and Sprint PCS at the 72-foot level. A security fence surrounds the existing 60-foot by 60-foot compound.  This fence will not be expanded.

Surrounding land uses consist of the Town’s public works garage, town offices, office and retail uses, and lumberyard. The zoning designation of this site is industrial.

The Town approved this tower at a height of 120 feet AGL. The Connecticut Historical Commission limited the height to 100 feet AGL to address concerns the tower had for the visual impact of the tower on the Suffield Historic District, particularly the Hatheway House located due east approximately 1,200 feet.  Since Crown and Cingular propose to increase the height of the tower, Crown and Cingular performed a crane test, raising the boom of a crane to a height of 110 feet AGL.  Susan Chandler of the Connecticut Historical Commission witnessed this test and determined that a height of 110 feet AGL will continue to meet the condition of the Memorandum of Understanding that the facility be fully obscured by vegetation from the Hatheway House.

Cingular has a need to be at the top of the tower to provide both coverage and capacity in Suffield; however, Council staff believes that the centerline height of antennas could be 102 feet which would maintain the ten-foot separation between carrier antennas, provides the necessary coverage, and minimizes the increase in tower height.  While Crown and Cingular would not object to such order, Cingular contends that the proposed 110-foot height would allow for optimum operation and Crown contends reducing the tower 5 feet would not allow for future shared use.

The worst-case power density for the telecommunications operations at the site has been calculated to be 42% of the applicable standard for uncontrolled environments.

Crown contends that the increase in height of this existing tower will not effect historical resources, will not result in a substantial environmental effect and does not require a certificate of environmental compatibility and public need.