Petition No. 552

Spectrasite

Bridgeport, Connecticut

Staff Report

April 1, 2002

On April 1, 2002, Connecticut Siting Council (Council) member Brian O’Neill and Robert Mercier of the Council staff met Spectrasite Communications, Inc. (Spectrasite) representative Julie Donaldson for an inspection of an existing Spectrasite monopole located at 1069 Connecticut Avenue in Bridgeport, Connecticut.  Spectrasite proposes to expand the compound lease area and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for the proposed lease expansion.

Spectrasite proposes to allow Northcoast Communications LLC (Northcoast) to locate at the 100-foot level of Spectrasite’s 132-foot monopole.  Northcoast would install nine panel antennas and equipment cabinets on a 10 x 20 concrete pad located east of the tower.  The existing fenced and graveled compound would be expanded approximately eighteen feet to the east to accommodate Northcoast’s equipment pad.  The existing 50-foot by 50-foot Spectrasite lease area is occupied entirely by the existing compound.

Under this petition, Spectrasite proposes to expand the lease area by approximately 900 square feet (50 feet by 18 feet) to accommodate Northcoast and a future telecommunications carrier.  The proposed expansion area consists of a level paved area in an existing parking lot.  An eight-foot tall chain link fence would enclose the proposed expanded compound.

The site is located in an urban commercial and residential area.  The site is zoned light industrial.  Site access and utility routing would be via established access and utility routes currently on site.

A structural analysis dated July 31, 2001 concluded that no additional reinforcement of the monopole or foundation is necessary for this proposal.  The worst case power density for the proposed telecommunications operations at the site has been calculated to be approximately 31% of the applicable ANSI standard for uncontrolled environments.

Spectrasite contends that the proposed lease expansion and site modification would not have a significant adverse environmental effect and therefore, would not require a Certificate.