Petition No. 571

Sprint PCS

Middletown, Connecticut

Staff Report

July 11, 2002

On July 10, 2002, Connecticut Siting Council (Council) member Gerald Heffernan and Fred Cunliffe of Council staff met Sprint representatives Thomas Regan, Jeff Gutowski, and Tina Marie Lopez for an inspection of an antenna installation on the roof of the boiler room building of the Middletown Electric Generating facility owned by NRG located at 1866 River Road, Middletown. Sprint proposes to modify the boiler room building for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for the proposed modification.

Sprint proposes to attach a total of 12 antennas, each measuring approximately 60 inches tall by eight inches wide by three inches deep, each supported by an approximately two-inch diameter by 66 inch long pipe extension mounted on the parapet of the boiler room roof.  Sprint proposes to install two sectors with antenna centerline radiation at 134 feet above ground level mounted on the east and west side of the boiler room roof.  Another sector would be installed on the south boiler room roof with antenna centerline radiation at 153 feet above ground level. Sprint would install power and communications cabinets on a 7-foot by 22-foot steel frame on the northwest corner of the boiler room roof.

The proposed site is an electric generating facility located in a remote area of Middletown along the Connecticut River.  The Department of Environmental Protection commented that bald eagles use trees on the shores of the Connecticut River for perching and feeding from December to March; however, Sprint’s proposal to install antennas on the generating building would have no effect on the bald eagles. The worst case power density for the proposed telecommunications operations at the site has been calculated to be approximately .05% of the applicable ANSI standard for uncontrolled environments.

Sprint contends that the proposed modification would not adversely affect the environment or ecology; would have no impact on scenic, historic, or recreational values; and therefore, would not require a Certificate.