Petition No. 590

Omnipoint Communications, Inc. d/b/a T-Mobile USA, Inc.

Windsor, Connecticut

Staff Report

November 7, 2002

On October 30, 2002, Connecticut Siting Council (Council) member Gerald Heffernan and Robert Mercier of the Council staff met with Omnipoint Communications, Inc (Omnipoint) representatives at a Connecticut Light and Power (CL&P) right-of-way south of Rood Avenue in Windsor, Connecticut for inspection of an electric transmission structure owned by CL&P.  Omnipoint, with the agreement of CL&P, proposes to modify the structure by installing antennas on a pipe mount and an equipment compound for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

Omnipoint proposes to install a 16-foot pipe mast on the existing 148-foot electric transmission line structure (no. 20073).  Two sets of three-panel antennas would be mounted at centerline heights of 155 and 161 feet above ground level (agl).  The total height of the structure would be 164 feet agl.

Three equipment cabinets would be installed on a 12-foot by 14-foot concrete pad enclosed within an 18-foot by 20-foot compound.  A six-foot high chain link fence would enclose the gravel compound area.  Access to the proposed site would be via a graded grassy track that would require minimal clearing.  Utility service would be provided from an underground conduit that would extend from an existing utility pole on Pine Line Extension, through a residential property to the right-of-way.

The tower location abuts a residential area to the south and west, Interstate 91 to the east and a continuation of the right-of-way to the north.  The right-of way contains two separate transmission lines and associated tower structures.  The proposed compound site is in a cleared area that would be visible from the backyards of several homes that directly abut the right-of-way.  In the petition, Omnipoint proposes to locate the compound access gate on the west side of the compound, in view of the residences.  Omnipoint would be willing to relocate the gate to the north side of the compound and establish vegetative screening on the west side to minimize potential visual impacts.

Omnipoint investigated the possible shared use of existing telecommunications facilities on Cottage Grove Road and Emerson Road in Windsor and determined coverage objectives could not be met.

The worst-case power density for the telecommunications operations at the site has been calculated to be 1.9% of the applicable standard for uncontrolled environments.

The proposed project is designed to provide coverage to coverage gaps on Interstate 91 in the vicinity of Exit 36.  Omnipoint contends that the proposed modification of the structure would not cause a substantial adverse environmental impact, and would prevent the construction of a new tower in the area.