Petition No. 594

AT&T Wireless PCS, Inc.

Meriden, Connecticut

Staff Report

November 21, 2002

On November 18, 2002, Connecticut Siting Council (Council) member Edward S. Wilensky and Christina Lepage of the Council staff met with AT&T Wireless PCS, Inc. (AT&T) representatives Harold Hewett, Nader Soliman, and Peter Carbone at 74 Birdsey Avenue, Meriden, Connecticut for inspection of an electric transmission structure. The structure is owned by Connecticut Light and Power (CL&P). AT&T, with the agreement of CL&P, proposes to modify the structure by installing antennas and associated equipment for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

AT&T proposes the installation of six panel antennas on an attachment above the existing monopole.  Three antennas would be installed at 164-feet above ground level (agl) and three antennas would be installed at 170-foot agl.  The installation of the proposed antennas on the existing 160-foot transmission line structure (#9403) would make the overall height at the top of the antennas 172-feet agl.

The proposed equipment would sit on a 6-foot by 5- foot 3-inch concrete pad within a 7-foot by 16-foot lease area.  A cable bridge would span from the equipment to the pole.  An 8-foot high chain link fence would surround the equipment compound.  Access to the proposed site would be via an existing paved area and dirt access road.  An underground conduit from an existing utility pole will provide power and telephone service to the site.

Construction activities would remain within the existing CL&P right-of-way over property that is owned by the Meriden Patrolman’s Benevolent Association.  Surrounding land uses include transmission towers, high voltage lines, right-of-way, residential, commercial, business and recreational facilities.  The zoning designation of this site is R-2 (residential).  Black Pond is located approximately 200 feet to the south of the existing monopole.

The worst-case power density for the telecommunications operations at the site has been calculated to be 0.4% of the applicable standard for uncontrolled environments.

AT&T would be willing to accept a condition that they be required to incorporate screening subject to City Planning Staff review and prior to the issuance of a building permit.

AT&T contends that the proposed modification of the structure would not cause a substantial adverse environmental impact, and would lessen the need for the construction of a new tower in the area.