## Petition No. 596

## Northeast Utilities

## Canaan, Connecticut

## December 19, 2002

~~~

On November 27, 2002, Northeast Utilities (NU) submitted a petition to the Connecticut Siting Council (Council) for a determination that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for modifications to the Falls Village Substation, off Water Street in Canaan, Connecticut.  The proposed route would be entirely within the fenced area of this substation.

On December 17, 2002, Colin C. Tait of the Council and Robert K. Erling of the Council staff met Kris Aberg of the Connecticut Light and Power Company (CL&P), the agent for NU, for a field review of this petition.

CL&P proposes to add two 115-kV circuit switchers which would be operated at 69-kV to 13.2 kV 5x transformer by installing two circuit switchers and associated voltage sensing equipment, effectively switching the 5x transformer over to an alternate 69 kV supply in case its normal supply is lost.  CL&P states this would improve system reliability and increase 13.2-kV substation capacity.  The proposed additions would be low profile in nature and impose little visual impact.  No wetlands or waterways would be affected.  Sound pressure levels would not change and would remain below state-regulated levels.