## Petition No. 641

## CL&P

## Wolcott, Connecticut

## August 26, 2003

~~~

On August 4, 2003, the Connecticut Light and Power Company (CL&P) submitted a petition to the Connecticut Siting Council (Council) for a determination that no Certificate of Environmental Compatibility and Public Need would be required for proposed modifications to CL&P's existing Todd Substation off of Todd Road in Wolcott, Connecticut.

On August 8, 2003, Edward Wilensky of the Council and Robert K. Erling of the Council Staff met Raymond L. Gagnon, James W. Borowitz, and Charles D. Ponte of CL&P for a field review of the proposed project at Todd Substation. The proposed work is needed to meet projected electrical loads in the area and would consist of the following: the installation of a 115-kV circuit breaker, and two 115-kV circuit switchers; the relocation of six 115-kV capacitive-coupled voltage transformers and two 115-kV transmission line wave traps; the installation of one 115 to 13.8-kV 47MVA power transformer and of 13.8 kV bus on steel structures; and the installation of 13.8-kV switchgear that would extend the existing 13.8 kV switchgear.

All of the proposed additions would be placed within the fenced areas of the substation which is cleared and contains considerable room for expansion and the placement of additional equipment. The area surrounding the substation is well screened by mature trees and brush; only one home was partially visible through trees from the substation. CL&P states that the sound levels along the property lines of the substation would continue to be in compliance with State regulations. The transformer to be installed would be provided with a sump capable of containing 110 percent of the transformer oil. Construction is proposed to begin in October 2003 and be completed by the end of June 2004.