Petition No. 650

The Connecticut Light and Power Company

Glenbrook Substation

Stamford, CT

Modifications

December 9, 2003

~~~

On October 29, 2003, the Connecticut Siting Council approved this petition for a tap of the existing 1977 line at Glenbrook Substation in Stamford, Connecticut by the Connecticut Light and Power Company (CL&P).  Included in the petition at that time was the temporary use of property at 153 Culloden Road and a driveway at 149 Culloden Road for construction access to this project.  Since that time, CL&P has been unable to successfully conclude negotiations with the owners of the property at 153 Culloden Road.  However, CL&P has been able to negotiate an agreement with the property owner at 149 Culloden Road to use their driveway and backyard, and with the owners of 145 Culloden Road for the use of their backyard and side yards for construction access.  Because of these changes, the tap structure would be moved approximately 57 feet to the south of its original location.  This change in location would enable CL&P to reduce the approach angle for the jack and bore from 92° to 90° from the rail road centerline.  Metro North prefers the angle be as close to 90° (perpendicular) as possible.  The new location of the jack and bore would avoid existing structures and increase the overall length of the tap by about 15 feet.  The design of the tap structure, jack and bore, and duct bank would not change.

Staff concludes these modifications are minor in nature and recommends approval of the modifications as detailed in CL&P’s letter and revised drawing dated November 14, 2003.