Petition No. 673

Omnipoint Communications, Inc. (T-Mobile)

347 East Street

Wolcott, CT

Staff Report

June 9, 2004

On May 28, 2004, Connecticut Siting Council (Council) member Edward S. Wilensky and Christina Lepage of the Council staff met with Omnipoint Communications, Inc., a subsidiary of T-Mobile USA, Inc. (T-Mobile) representative Stephen Humes at 347 East Street, Wolcott, Connecticut for the inspection of an existing lattice tower.  The structure is owned by Crown Castle.  T-Mobile proposes to modify the existing tower by installing antennas and associated equipment for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

T-Mobile proposes to install six flush mounted antennas, which would be mounted to pipe supports attached to the existing 180-foot tower.  The pipe mast would extend approximately ten feet above the top of the existing tower.  The antennas would be mounted with a centerline at 188 feet above ground level (AGL) bringing the top of the tower to 190 feet three inches AGL.  T-Mobile would install GPS and GSM antennas on the ice bridge at 30 feet AGL.

The proposed equipment would be installed on a 17-foot by five-foot concrete slab to be located within the existing fenced area at the base of the tower.  Access to the tower is via an existing access drive extending from East Street.  Utilities would originate from existing sources.

The tower is located in an industrial zone on property owned by Agostino Rodrigues.  The proposed antennas are intended to provide coverage to a portion of Interstate 84, Route 322 and the surrounding area.

The calculated cumulative worst-case radio frequency power density would not exceed the applicable standard.

T-Mobile contends that the proposed project would reduce the need for another telecommunications tower to provide coverage to the area, and that the proposed project would not have a substantial environmental effect.