Petition No.771

Cingular

652 River Road (State Route 12), Lisbon

June 6, 2006

Cingular is seeking to replace an existing, 93-foot tall laminated wood transmission line tower with a similar structure that would be 108 feet tall. Cingular would install 12 antennas on T-arm mounts at a centerline height of 105 ½ feet.

Council member Jerry Murphy and staff member David Martin conducted a field review of this petition on June 5, 2006. Cingular was represented by Lucia Chiocchio, an attorney with Cuddy & Feder, Carlo Centore, an engineer with  Natcomm, and Tim Burks of Cingular.

The CL&P transmission line in this area runs north-south and intersects River Road (State Route 12 at a slight angle. The transmission tower to be replaced is approximately 200 feet south of River Road. Cingular would build a gravel drive to access the tower. Its ground equipment would be housed in an 11’ 6” by 20’ equipment shelter within a 24’ by 30’ fenced compound.

The replacement tower would be designed to accommodate only one carrier.

The tower is located on a 21-acre parcel owned by CL&P. The vicinity of the tower is characterized by scattered residential development. The nearest residence is 295 feet to the northeast of the tower. However, this residence is unlikely to have a view of the tower due to topography and the presence of numerous mature, deciduous trees along the edges of the right-of-way. Views of the tower appear to be limited to River Road for the short interval CL&P has cleared for the transmission line.

Staff calculates that the power density for Cingular’s antenna array would be 0.0988 mW/cm2 which represents 13.92% of the FCC’s maximum permissible exposure.

View of tower to be replaced