Petition 780

Connecticut Light and Power

Plumtree Substation, Bethel

Staff Report

August 31, 2006

On July 24, 2006, the Connecticut Light and Power Company (CL&P) submitted a Petition (Petition) for a declaratory ruling that no certificate of environmental compatibility and public need is required for the proposed modifications to the Plumtree Substation, Bethel.  Specifically, CL&P seeks to: install one permanent 115-kV oil-filled circuit breaker and associated switch; install one 115-kV circuit breaker and associated switch as a mobile position to connect a transformer in the event of an outrage; install one 115- to 13.8-kV, 46.7 Megavolt ampere (MVA) power transformer and associated equipment and install one 13.8-kV switchgear enclosure.  This proposed work is not associated with the Docket No. 217 Bethel-Norwalk 345-kV Transmission line..

The purpose of the project is to meet increased loads and improve distribution reliability. The proposed breakers and connections to the 115-kV bus would occur at the existing height.  There would be no increase in equipment height at the substation.  No expansion of the fence line is necessary.

On August 15, 2006, Council member Edward S. Wilensky and Fred Cunliffe of Council staff met with Chuck Ponte, Project Engineer and Ben Fishman, CL&P intern.

The substation is located in a residential area, well screened by vegetation, and the compound is not visible to adjacent residences.

If approved, CL&P anticipates that construction would begin during September 2006 with expected completion by May 2007.