Petition 789

Connecticut Light and Power

Stony Hill Road, Brookfield

Staff Report

September 28, 2006

On Monday, September 25, 2006, Connecticut Siting Council (Council) member Gerald T. Heffernan and Christina Lepage of the Council staff met with the Connecticut Light and Power Company (CL&P) representative Robert J. Charpentier, P.E. to review a Petition (Petition) for a declaratory ruling that no certificate of environmental compatibility and public need is required for the proposed modifications to the Stony Hill Substation, Brookfield.  Specifically, CL&P proposes to install on one 115-kV motor-operated disconnect switch and one circuit switcher to allow temporary connections of a mobile transformer.

The proposed installation is required to increase the capacity rating of the substation and to meet projected peak load requirements.

The substation is fed from two 115-kV transmission lines and two step-down transformers are used to serve local distribution.

The proposed construction would be within the fenced area of the Stony Hill Substation.  The height of the additional equipment would be 21 feet 6 inches, which is less than the height of the existing structures.  The proposed project would have minimal visual impact because the additional equipment would be similar to existing equipment at the substation.  The substation is not within a 100-year flood zone or stream channel encroachment lines.  Wetlands and waterways would not be impacted.

CL&P expects to begin construction on the proposed modification to the substation in May of 2007 and complete construction by December of 2007.