Petition No. 851

Dominion Nuclear Connecticut, Inc.

Waterford, CT

Staff Report

April 24, 2008

On April 8, 2008, Connecticut Siting Council (Council) member James J. Murphy, Jr. and Derek Phelps of Council staff met Thomas J. Bransfield, Engineer III, and associated staff Forrest A. Kocon, Dennis R. Latz, and J. David Dakers, P.E. of Dominion Nuclear CT at Millstone Power Station, Waterford, Connecticut.  Dominion Nuclear CT. Inc. (Dominion) is petitioning the Council that neither a new Certificate of Environmental Compatibility and Public Need (Certificate) nor a modification of the existing Certificate is required to replace and relocate two existing auxiliary boiler fuel tanks and to relocate the existing sandblasting facility building at Millstone Power Station (Millstone) in Waterford, Connecticut.

DNC currently maintains two (2) 25,000 gallon underground fuel oil tanks located to the east of Building No. 303 and adjacent to the Unit 3 substation.  These tanks store fuel oil for the Unit 3 auxiliary boiler.  The tanks have been in service since 1983 and are due to be replaced.  However, because of the location of the Unit 3 Output Breaker and the associated structural support frame above the tank, Dominion is unable to access the area in order to remove and replace the tanks.

As an alternative to replacing the existing tanks, Dominion wishes to install one new 50,000 gallon fuel tank on a concrete pad adjacent to and east of Building No. 305.  Once the new tank is installed and tested to ensure suitable operation, the existing underground tanks will be abandoned in place in accordance with Connecticut Department of Environmental Protection Regulations.

The location of the new tank, however, requires the relocation of an existing sandblasting facility.  Therefore, Dominion wishes to develop a new 1,000 square-foot (20’ x 50’) pre-engineered open-span metal building, constructed on a concrete pad.  The new sandblasting building would be constructed in an open area adjacent to and immediately south of Building No. 454.

The field review confirmed that the auxiliary boiler fuel oil tank replacement project and the relocation of the sandblasting facility building will not involve significant alteration in the physical or environmental characteristics of the property.  All construction will occur in previously-disturbed areas and will be located completely within the protected area.  Thomas V. Wagner, Planning Director for the Town of Waterford submitted a letter in support of these proposed modifications dated August 29, 2007.  Staff recommends approval.