Petition No. 854

PPL SavageAlert on behalf of Veolia Water North America-Northeast LLC

Naugatuck, CT

Staff Report

April 24, 2008

On April 17, 2008, Connecticut Siting Council (Council) member Edward S. Wilensky and Christina Lepage of the Council staff met with Philip J. Fine and Christian Hoan of Veolia Water North America – Northeast LLC (Veolia) at the proposed site.

PPL SavageAlert (PPL) submitted a Petition for Declaratory Ruling on behalf of Veolia for the installation of an ORMAT Energy Converter (OEC) to be located at the Naugatuck Wastewater Treatment Facility at 500 Cherry Street in Naugatuck, CT.  PPL and Veolia entered into an agreement for the installation of an OEC that will use waste heat from the fluidized bed incinerator as the heat source for the electric power generation system.

ORMAT Technologies, Inc. had applied to the Department of Utility Control (DPUC), in Docket 07-06-07, for a declaratory ruling that the OEC system would qualify as a Class I renewable energy source that meets the definition of “low emission advanced renewable energy conversion technology” in accordance with Connecticut General Statutes § 16-1(26).  On August 15, 2007, the DPUC issued a Decision stating that the system would qualify as a Class I renewable energy source but the owner or authorized agent would need to apply for a Connecticut Class I registration prior to commencement of operation.

The proposed OEC would produce a maximum of 350 kW of electricity.

The OEC would be installed outdoors, adjacent to the building that contains the fluidized bed incinerator.  The equipment would be skid mounted and approximately 7.5 feet wide by 21 feet tall by 42 feet in length.

Part of the cost of installation of the proposed OEC would be funded by Connecticut Innovations, Inc., acting as the administrator of the Renewable Energy Investment Fund also known as the Connecticut Clean Energy Fund.

PPL seeks a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required.