Petition No. 884

The Connecticut Light and Power Company

Portland

February 19, 2009

Staff Report

On January 14, 2009, the Connecticut Siting Council (Council) received a Petition (Petition) from The Connecticut Light and Power Company (CL&P) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required for the proposed removal of a single-circuit 115-kV transmission line segment in Portland.  Specifically, CL&P would remove 16 wood H-frame transmission structures, including the conductors, overhead shield wires, poles, guy wires, etc. on a 1.3 mile de-energized transmission line segment (#1767) between Portland Substation and Ames Junction in Portland.  The existing energized #1759 transmission line in the same right of way would remain.  The right of way is owned by CL&P.

CL&P seeks to remove the line segment because it has been de-energized for a considerable amount of time and is not need for electric reliability.  In addition, CL&P believes it is a safety hazard to have a de-energized line adjacent to an energized line due to possible stray voltages.

The wood poles, pole butts, and wood cross-arms would be removed entirely and disposed of in accordance with best management practices for disposal of treated wood poles.    All line conductors, shield wires, insulators and hardware would be remove and disposed of or recycled in accordance with best management practices.

The clearing required for the proposed removal work would be similar to the mowing and clearing that is conducted every fourth year on this right of way section.  CL&P notes that this would be necessary to ensure the stability of construction mats and safe operation of the equipment.

CL&P would avoid work within wetlands to the extent possible by utilizing multiple existing right of way access points to gap wetlands.  CL&P would only have to cross one wetland (Wetland #2) to complete its work.  CL&P would minimize wetland disturbance by using construction mats to support the necessary equipment.  The mats would be removed and any disturbed area would be restored.  Approximately 400 square feet of wetland would be temporarily matted during the project, but not clearing of wetland vegetation is anticipated.  CL&P would apply suitable soil and erosion controls.

Based on a review of the DEP’s Natural Diversity Database, no state or federally endangered, threatened, or state special concern species have been identified on the property.

This Petition was field reviewed on February 11, 2009 by Council member Brian Golembiewski and Fred Cunliffe and Michael Perrone of the Council staff.  Five representatives of CL&P also attended the field review: John Morissette, Manager – Transmission Siting and Permitting; Mick Collins, Field Planner – Transmission; Louis Rubano, Project Manager – Transmission Projects; Steve Osuch, Assistant Engineer – Transmission Projects; and Susan Provost, Associate Scientist.

If approved, CL&P anticipates approximately three months of work would be required for this project.  CL&P proposes to commence this project in May 2009 with completion of work expected no later than the end of 2010.  This is because this project may be delayed by CL&P due to other higher priority work e.g. work involving line outages.