Petition No. 903

The Connecticut Light and Power Company

Montville Switching Station

August 13, 2009

Staff Report

On June 4, 2009, the Connecticut Siting Council (Council) received a Petition from The Connecticut Light and Power Company (CL&P) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required for modifications to CL&P’s Montville switching station located on Lathorp Road in Montville.  Council member Brian Golembiewski and staff member Robert Mercier visited the site on August 4, 2009 to review the proposal. CL&P representatives Helen Taylor, Beverly Peters, and others, attended the field review.

CL&P proposes to install a transformer at the Montville switching station to serve as a spare, if needed, for the Montville, Card Street, or Southington substations.  The 400 MVA transformer would be placed on a 43-foot by 29-foot concrete pad in the southeast corner of the substation.  The installation would require the removal of approximately 250 cubic yards of soil.

The installation would have no effect on environmental resources.  The location is within a developed, graveled compound adjacent to NRG’s Montville Power Station.  Excavated soil would be environmentally tested prior to disposal.  A containment system designed to capture 110% of the unit’s transformer oil would be installed during pad construction.  The transformer would not be visible from adjacent private property.