Petition No. 923

FuelCell Energy, Inc.

539 Technology Park Drive, Torrington

Staff Report

December 3, 2009

On November 6, 2009, the Connecticut Siting Council (Council) received a Petition (Petition) from FuelCell Energy, Inc. (FCE) for a Declaratory Ruling that No Certificate of Environmental Compatibility and Public Need is required for the testing of newly manufactured fuel cells at 539 Technology Park Drive, Torrington.

Three different size fuel cells are manufactured by FCE: 300 kilowatt (kW); 1.4 megawatt (MW); and 2.8 MW.  An installation would include the fuel modules, associated electrical equipment, main process skid, desulfurization skid, and water treatment skid.  The project area is already surrounded by a six-foot height chain link fence.  Natural gas would be the fuel source.  Natural gas service exists at the site and is supplied by Yankee Gas.

The nearest residence is approximately 515 feet to south of the proposed test facility site.  The visual and noise impacts are not expected to be significant given that existing industrial buildings and mature tree cover surrounding the area.  The project is expected to meet all applicable noise standards at the property line.

There are no wetlands or water bodies in the vicinity of the proposed site.  No new land would be cleared for the project.  The largest unit, 2.8 MW, would consume just under 13,000 gallons of water per day via the municipal water system, and wastewater would be discharged via the existing sewer system.  The relatively low air emissions associated with even the largest unit are low enough such that no registrations or applications are required from the Connecticut Department of Environmental Protection.

One thousand five-hundred liters of nitrogen would stored at the site for use in the fuel cell process.  Nitrogen is environmentally benign since air is approximately 78 percent nitrogen.  It would be securely stored in a cylinder on its own concrete pad inside the fenced compound.

The project is already in place because past testing did not involve the sale of electricity to the grid.  Since these larger units would result in an electrical surplus that could be sold to the grid, FCE seeks approval for ongoing testing.  One system would be tested at time (for about 2 to 3 months) and then shipped to a customer.  Testing would continue on an ongoing basis depending on sales to customers.  The size of the units would vary, but is not expected to exceed 2.8 MW.  As technology advances and output increases, staff recommends that FCE notify the Council in the event that any unit being tested has an output exceeding 3 MW.

Abutting property owners and the City of Torrington have been noticed.  No objections have been received.  This petition was field reviewed by Council Member Colin Tait and Michael Perrone of the Council Staff on December 2, 2009.  Attorney Joey Lee Miranda, Robinson & Cole LLP, representing FCE also attended the field review along with two representatives from FCE: Kirk Arneson, Senior Project Manager; and Anthony J. Leo, Vice President – Applications and OEM Engineering.