Petition No. 936

The United Illuminating Company

Milford, Connecticut

Staff Report

April 8, 2010

On March 18, 2010, the Connecticut Siting Council (Council) received a petition from The United Illuminating Company (UI) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the proposed modification to the existing transmission facility in Milford.  On March 30, 2010, Council member Philip T. Ashton and Christina Walsh of the Council staff met with UI representatives Bohdan Katreczko and Brad Parsons.

The Connecticut Department of Transportation (CDOT) is reconstructing the Moses Wheeler Bridge along Interstate 95, which extends over the Housatonic River.  The bridge will be widened approximately 45 feet to the north and would conflict with the existing UI transmission line.  Structure number B864 would be relocated to make room for the bridge reconstruction.  Preliminary engineering for this project has been approved by CDOT and the State of Connecticut would pay the cost of the structure relocation.

The existing structure B864 is a 70-foot steel catenary support structure, which is part of a 115-kV transmission line running along the Metro North Railroad from southwest to northeast.  UI proposes to remove the existing structure and replace it with a new 75-foot monopole approximately 80 feet east of the original location and 40 feet north of the bridge.

UI’s proposed construction is within the existing transmission line right-of-way.

UI’s construction would begin in September 2010 and take approximately six weeks to complete.

UI states that the proposed project would not have a substantial adverse environmental effect and, therefore, would not require a Certificate.