Petition No. 943

UTC Power Corporation

Torrington, Connecticut

Staff Report

May 6, 2010

On April 22, 2010, the Connecticut Siting Council (Council) received a petition from UTC Power Corporation (UTC Power) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required for the installation of a 400 kW fuel cell in Torrington.  On April 30, 2010, Council member Colin C. Tait and Christina Walsh of the Council staff met with UTC Power representatives Kent McCord and Jason Charles to conduct a field review of the proposed installation.

UTC Power proposes to install a fuel cell at 931 Torringford Street in Torrington on the site of a future Stop & Shop supermarket that is presently under construction.  The proposed fuel cell is 9 feet wide by 29 feet long by 10 feet tall and would be located immediately behind the Stop & Shop building.  The equipment would be completely enclosed.

The proposed installation is a natural gas-fueled, phosphoric acid fuel cell system.  The fuel cell is a distributed generation resource and combined heat and power application that would provide electric power while using waste heat for heating and cooling.  The fuel cell would provide the supermarket with approximately 90 % of its electricity needs.  The unit would continue to provide service to the supermarket even when electric service fails.

The proposed fuel cell would operate in water balance, meaning that water would not be added or discharged after initial start-up of the facility under normal operating circumstances.  If any water overflow from the unit occurs, it would consist of de-ionized water and flow directly into a sanitary drain.  The unit would meet all Connecticut Department of Environmental Protection air and water quality standards.

The area surrounding the site of the fuel cell is commercial: no homes are in the vicinity.  Nevertheless, the fuel cell would be contained within a painted metal enclosure and surrounded by a wood fence, which would minimize visual impacts.  Noise emissions would be at a level compatible with commercial uses and limited to a short distance (60 dB at 33 feet): the nearest residential receptors are at approximately 10 times that distance.

UTC Power met with Brett Zuraitis, Building Official for the City of Torrington on February 18, 2010.  Mr. Zuraitis did not express concerns about the proposed installation.