Petition No. 951

Connecticut Light & Power Company

Southington, Connecticut

Staff Report

June 17, 2010

On May 27, 2010, the Connecticut Siting Council (Council) received a petition from The Connecticut Light & Power Company (CL&P) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required for proposed modifications to the Southington substation in Southington, Connecticut. Council member Ed Wilensky visited the site with staff member David Martin on June 10, 2010 to review the proposal. Bob Charpentier, Chris Kasamba, and John Morissette represented CL&P at the field review.

CL&P’s proposed modifications consist of replacing a section, approximately 170 feet in length, of the chain link fence that encloses the substation. The section of fence to be replaced is approximately five feet high, which is lower than the 2007 National Electrical Safety Code’s requirement for substation fences to be at least seven feet high. It would be replaced by a seven-foot high fence with one foot of barbed wire on top. The section of fence to be replaced runs parallel to Belleview Avenue and includes the front gate to the substation. This area of the substation is well-screened from Belleview Avenue by existing, mature vegetation.

The proposed fence replacement should not create any significant adverse environmental impacts.