Petition No. 955

Clearwire

New Haven, Connecticut

Staff Report

August 17, 2010

On July 1, 2010, the Connecticut Siting Council (Council) received a petition from Clear Wireless LLC (Clearwire) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required for the addition of a ten-foot extension to an existing 76-foot tall monopole tower located at 389 Forbes Avenue in New Haven, Connecticut. Council member Dr. Barbara Bell visited the site with staff member David Martin on July 23, 2010 to review the proposal. Jennifer Herz, a lawyer with Brown Rudnick, and Paul Fanos, an engineer with Infinigy Engineering & Surveying, represented Clearwire at the field review.

The existing tower was approved at 66 feet under Docket 298 on February 2, 2005. It replaced a billboard on which Sprint had mounted antennas on an adjacent property at 401-411 Forbes Avenue. The replacement was necessitated by the reconstruction of I-95, a project that resulted in the condemnation of the 401-411 Forbes Avenue property. There are three carriers on the existing tower: Sprint at a centerline height of 62.5 feet, T-Mobile at 55 feet, and Pocket at a centerline height of 72 feet. Pocket received approval on July 22, 2009 from the Council under Petition 908 to extend the height of the tower to 76 feet in order to place its antennas at its current height.

Now Clearwire would like to extend the tower an additional ten feet in order to install three WiMAX antennas, three remote radio heads, and four microwave dishes. Clearwire’s antennas would be installed on T-arm mounts. These mounts, however, would not extend as far out from the tower as the mounts of Sprint and T-Mobile, nor would they be as wide, making Clearwire’s visual profile smaller than the two lowest carriers. Pocket’s antennas are flush-mounted. Clearwire’s ground equipment would be installed inside a seven-foot by seven-foot leased area within the existing compound.

A structural analysis of the tower concluded that it could support the proposed extension and additional antennas. Council staff calculates that the addition of Clearwire’s antennas would bring the aggregate power density of the tower’s existing antenna arrays to 54.8% of the FCC’s Maximum Permissible Emission.

The existing tower is located towards the rear of its host property—a gas station/convenience store—approximately 70 feet from Forbes Avenue (Route 1) and 30 feet from the retaining wall at the edge of the I-95 right-of-way. The immediate vicinity of the site consists mostly of commercial and industrial uses, although there is a small side street with four residences directly across Forbes Avenue from the tower site. There are a number of tall 345 kV transmission towers in the near vicinity and an industrial smoke stack across I-95, so this tower would not be a singular vertical intrusion on the heavily urbanized viewscape.

The proposed extension of this existing tower is not expected to have any substantial adverse environmental effects.