ITEM #1105001A   -   1 WAY, 1 SECTION SPAN WIRE TRAFFIC SIGNAL

ITEM #1105003A   -   1 WAY, 3 SECTION SPAN WIRE TRAFFIC SIGNAL

ITEM #1105006A   -   2 WAY, 1 SECTION SPAN WIRE TRAFFIC SIGNAL

ITEM #1105007A   -   2 WAY, 3 SECTION SPAN WIRE TRAFFIC SIGNAL

ITEM #1105011A   -   3 WAY, 3 SECTION SPAN WIRE TRAFFIC SIGNAL

ITEM #1105014A   -   4 WAY, 1 SECTION SPAN WIRE TRAFFIC SIGNAL

ITEM #1105015A   -   4 WAY, 3 SECTION SPAN WIRE TRAFFIC SIGNAL

ITEM #1105101A   -   1 WAY, 1 SECTION MAST ARM TRAFFIC SIGNAL

ITEM #1105103A   -   1 WAY, 3 SECTION MAST ARM TRAFFIC SIGNAL

ITEM #1105107A   -   2 WAY, 3 SECTION MAST ARM TRAFFIC SIGNAL

ITEM #1105180A   -   1 WAY, 1 SECTION BI-COLORED ARROW

ITEM #1105203A   -   1 WAY, 3 SECTION POLE MOUNTED TRAFFIC SIGNAL

ITEM #1105303A   -   1 WAY, 3 SECTION PEDESTAL MOUNTED TRAFFIC signal

item #1105490a – 1 way, 1 section traffic signal sign mounted

SECTION 11.05 – TRAFFIC SIGNALS is amended and supplemented as follows:

Article 11.05.02 – Materials:

Amend as follows:

Article M.16.06 - Traffic Signals

Sub Article 3 - Housing:

In the last sentence of the third paragraph, between the words “housing” and “shall” add “and all internal hardware”.

Add the following after the last paragraph:

Each section of the housing shall be provided with a removable visor. The visor shall be the cap type, unless otherwise noted on the plan. The visor shall be a minimum 0.05 inch thick. The visor shall be the twist on type and secured to the signal by four equidistant flat tabs screwed to the signal head. The visor shall fit snugly against the door and shall not permit any perceptible filtration of light between the door and visor.

Sub Article 4 - Brackets:

Remove the second paragraph.

Replace the last paragraph with the following:

When indicated on the plans, a backplate constructed of 5052-H32 aluminum alloy sheet between 0.050-inch to 0.065-inch thickness meeting the requirements of ASTM B209 shall be attached to the signal head housing. The front surface of backplate per MUTCD requirements shall have a dull black finish to minimize light reflection and to increase contrast between the signal indication and its background.

Backplates shall be 5 inches wide and louvered.

Install a 2 inches wide fluorescent yellow retroreflective strip (Type XI sheeting) along the perimeter of the face of the backplate.

Sub Article 5 – Optical Unit and Sub Article 6 – Lamp Socket Delete both subarticles and replace with the following:

Optical Unit, Light Emitting Diode:

(a) General:

Only Optical Units that meet the requirements contained herein, supplied by the manufacturers noted below or approved equal, will be accepted.  Final review of model numbers will be done at the time of the product data submittals.

Dialight 					Leotek

1501 Foute 34 South				726 South Hillview Drive

Farmingdale, NJ 07727			Milpitas, CA 95035

The materials for Light Emitting Diode (LED), Optical Unit, circular and arrow, shall meet the following requirements:

- The ITE Performance Specification for Vehicle Traffic Control Signal Heads – Light Emitting Diode (LED) Circular Signal Supplement for circular indications dated June 27, 2005.

- The ITE Performance Specification for Vehicle Traffic Control Signal Heads – Light Emitting Diode (LED) Vehicle Arrow Traffic Signal Supplement for arrow indications dated July 1, 2007.

- Military grade connectors.

- Circular indications shall have a 20-year design life conformal coated driver board

- Solid connection between driver board and LED light engine for enhanced corrosion resistance

- Robust solder joints on the back of the printed circuit board.

- The optical unit for circular indications shall exceed ITE mandated light intensity for over 15 years. Specific model numbers ITE compliant listed with ETL Intertek

- Sealed against dust and moisture intrusion per Mil-Std-810F Method 506.4, Procedure 1 – Rain and Blowing Rain.

- LED unit shall have an incandescent appearance, not pixelated, when illuminated.

- Non-electrolytic capacitors to prevent failure from drying out

- The LED unit shall have a manufacturer-provided warranty of 15 years from the date of delivery

- The LED unit for bi-colored arrow and U-turn arrow indications shall have a manufacturer-provided warranty of 60 months from the date of delivery

Section 4, Adjustable Traffic Signals and General Housing sections of the CT Department of Transportation Functional Specifications for Traffic Control Equipment, current edition governs. Where the Department of Transportation Functional Specifications conflict with this Special Provision or the 2005/2007 ITE Performance Specifications, this Special Provision and the 2005/2007 ITE Performance Specifications shall govern.

The Optical Unit shall have an Incandescent look and shall be made up of a smooth surfaced outer shell. The Optical Unit shall have multiple LED light sources, a filtered power supply and a back cover, assembled into a sealed unit.  The Optical Unit shall be certified as meeting the current ITE Specifications by Intertek Testing Services, Inc. (ITSNA, formerly ETL) or another organization currently recognized by the Occupational Safety and Health Administration (OSHA) as a Nationally Recognized Testing Laboratory.  The Optical Unit shall perform to the requirements of the ITE Specification for a minimum of 15 years. The Optical Unit for bi-colored arrow indications shall perform to the requirements of the ITE Specification for a minimum of 60 months.

The Arrow Optical Unit shall be “Omni-Directional” so that it may be oriented in any configuration without degradation of performance.

(b) Electrical Requirement:

Operating voltage:

- 80 to 135 Volts AC with cutoff voltage (no visible indication) below 35Volts AC.

Power requirements:

- Circular Indications:  12 inch - no more than 13 Watts

- Circular Indications:  8 inch - no more than 7 Watts

- Arrows Indications:  12 inch - no more than 13 Watts

Power Supply:

- Fused and filtered to provide excess current protection and over voltage protection from electrical surges and transient voltages.

(c)  Photometric Requirement:

Beam Color:

- Meet current ITE Specifications

(d)  Mechanical Requirements:

Diameter:

- The Circular Optical Unit shall fit into standard 12 inch or 8-inch housing.  The Arrow Optical Unit shall fit 12-inch housings only.

Enclosure:

- Clear lens cover for all Red, Yellow and Green Circular Optical Units.

- Incandescent appearance, not pixelated, when illuminated.

- For Arrow Optical Units the arrow indication segment of the lens shall be clear.

- Enclosure sealed and waterproofed to eliminate dirt contamination and be suitable for installation in all weather conditions.

- Clearly mark on the housing the following information:

  - Manufacturer & model number

  - Date of manufacture

- The model number shall end with the number of LEDs used to comprise the unit as the last digits of the model number.  For example, if the unit is comprised of 3 LEDs and the model is x12y, then the new model number shall read x12y3.

Operating temperature:

- Meet current ITE Specifications

Wiring: LED lamps shall have color coded 16 AWG wires for identification of heads as follows:

| RED LED Lamps | RED with WHITE neutral |
| --- | --- |
| YELLOW LED Lamps | YELLOW with WHITE neutral |
| GREEN LED Lamps | GREEN or BROWN with WHITE neutral |
| RED LED ARROWS | RED/WHITE with WHITE neutral |
| YELLOW LED ARROWS | YELLOW/WHITE with WHITE neutral |
| GREEN LED ARROWS | GREEN/WHITE or BROWN/WHITE with WHITE neutral |
| GREEN/YELLOW LED ARROWS | GREEN/WHITE or BROWN/WHITE, YELLOW/WHITE, with WHITE neutral |

- Wires shall be terminated with a Block Spade, 6-8 stud/ 16-14 wire size.

- All Circular Optical Units shall be supplied with a minimum 40-inch long pigtail and all Arrow Optical Units shall be supplied with a minimum 60-inch long pigtail.

Delete Sub Article 8 – Dual Color Fiber Optic Section

Article 11.05.03 – Construction Methods:

Add the following paragraph:

Circular indications that have an identification mark (such as an arrow) on the top of the lens shall be installed with that mark at the 12 o-clock position.