Summary of the Fit Test Procedure for N95 respirators:

Qualitative with Sweet (saccharin) or Bitter (BitrexTM)

This procedure is summarized in OSHA’s respiratory protection standard (29 CFR 1910.134) Appendix A - Qualitative Fit Test Protocols- Sections B3 and B4.  In addition, the manufacturers of fit test kits have detailed fit test procedure instructions as well as fit test videos online

I.  Preparation

1.	Pour a small amount (approximately one tsp.) of the Sensitivity Test Solution (#1) into the nebulizer labeled “#1 Sensitivity Test Solution.”

2.	Pour the same amount of Fit Test Solution (#2) into the second nebulizer labeled

“#2 Fit Test Solution.”

3.	Recap the bottles.

II.  Sensitivity Test

This test is done to assure that the person being fit tested can detect the taste of the test solution at very low levels. The Sensitivity Test Solution is a very dilute version of the Fit Test Solution.  The test subject should not eat, drink (except water), or chew gum for 15 minutes before the test.

1.	Have the test subject put on the hood without a respirator.

2.	Position the hood forward so that there is about six inches between the subject’s face and the hood window.

3.	Instruct the test subject to breathe through his/her mouth with tongue extended.

4.	Using Nebulizer #1 with the Sensitivity Test solution (#1), inject the aerosol into the hood through the hole in the hood window.  Inject 10 squeezes of the bulb, fully collapsing and allowing the bulb to expand fully on each squeeze. Both plugs on the nebulizer must be removed from the openings during use. The nebulizer must be held in an upright position to ensure aerosol generation.

5.	Ask the test subject if s/he can detect the taste of the solution. If tasted, note the number of squeezes as 10 and proceed to the Fit Test.

6.	If not tasted, inject an additional 10 squeezes of the aerosol into the hood.  Repeat with 10 more squeezes if necessary. Note whether 20 0r 30 squeezes produced a taste response.

7.	If 30 squeezes are inadequate, in that the subject does not detect a taste, the test is ended. Another type of fit test must be used.

8.	Remove the test hood, and give the subject a few minutes to clear the taste from his/her mouth. It may be helpful to have the subject rinse his/her mouth with water.

III.  Fit Test

1.	Have the test subject don the respirator and perform a user seal check per the instructions provided on the respirator package.

2.	Have subject wear any applicable safety equipment that may be worn during actual respirator use that could interfere with respirator fit.

3.	Have subject put on and position the test hood as before, and breathe through his/her mouth with tongue extended.

4.	Using Nebulizer #2 with Fit Test Solution (#2), inject the fit test aerosol using the same number of squeezes as required in the Sensitivity Test (10, 20, or 30). A minimum of ten squeezes is required, fully collapsing and allowing the bulb to expand fully on each squeeze. The nebulizer must be held in an upright position to ensure aerosol generation.

5.	To maintain an adequate concentration of aerosol during this test, inject one-half the number of squeezes (5, 10, or 15) every 30 seconds for the duration of the fit test procedure.

6.	After the initial injection of aerosol, ask the test subject to perform the following test exercises for 60 seconds each:

- Normal breathing – In a normal standing position, without talking, the subject shall breathe normally.

- Deep breathing – In a normal standing position, the subject shall breathe slowly and deeply, taking caution not to hyperventilate.

- Turning head side to side – Standing in place, the subject shall slowly turn his/her head from side to side between the extreme positions on each side. The head shall be held at each extreme momentarily so the subject can inhale at each side.

- Moving head up and down – Standing in place, the subject shall slowly move his/her head up and down. The subject shall be instructed to inhale in the up position (i.e., while looking toward the ceiling).

- Talking -- The subject shall talk out loud slowly and loud enough so as to be heard clearly by the test conductor. The subject can read from a prepared text such as the Rainbow Passage, count backward from 100, or recite a memorized poem or song.

Rainbow Passage:  When the sunlight strikes raindrops in the air, they act like a prism and form a rainbow. The rainbow is a division of white light into many beautiful colors. These take the shape of a long round arch, with its path high above, and its two ends apparently beyond the horizon. There is, according to legend, a boiling pot of gold at one end. People look, but no one ever finds it. When a man looks for something beyond reach, his friends say he is looking for the pot of gold at the end of the rainbow.

- Bending over – The test subject shall bend to the waist as if he were to touch his/her toes.  Jogging place may be substituted for this exercise.

- Normal breathing – same as exercise “a”

  - The test is terminated at any time the sweet taste of aerosol is detected by the subject because this indicates and inadequate fit.  Wait 15 minutes and perform the sensitivity test again.

  - Repeat the fit test after re-donning and readjusting the respirator. A second failure may indicate that a different size or mol\del respirator is needed.

  - If the entire test is completed without the subject detecting the sweet taste of the aerosol, the test is successful and the respirator fit has been demonstrated.

  - Periodically check the nebulizer to make sure that it is not clogged. If clogging is found, clean the nebulizer and retest.

Rainbow Passage

When the sunlight strikes raindrops in the air, they act like a prism and form a rainbow.  The rainbow is a division of white light into many beautiful colors.  These take the shape of a long round arch, with its path high above, and its two ends apparently beyond the horizon. There is, according to legend, a boiling pot of gold at one end. People look, but no one ever finds it.  When a man looks for something beyond reach, his friends say he is looking for the pot of gold at the end of the rainbow.