Existing Coverage

| Route | ( -75 dbm | ( -90 dbm | Gap < -90 dbm | Total Miles |
| --- | --- | --- | --- | --- |
| 49 | 0.0 | 2.3 | 6.0 | 8.3 |
| 138 | 1.0 | 5.7 | 2.6 | 8.3 |
| 165 | 0.8 | 4.7 | 4.0 | 8.7 |
| 201 | 3.5 | 5.7 | 1.9 | 7.6 |

(Cellco 11, Q. 18, maps)

- Placing Cellco antennas on the proposed prime site tower at a point 150 feet AGL would provide the following coverage within a four mile radius of the proposed prime site:

Proposed Prime Site Tower

| Route | ( -75 dbm | ( -90 dbm | Gap < -90 dbm | Total Miles |
| --- | --- | --- | --- | --- |
| 49 | 4.3 | 8.3 | 0.0 | 8.3 |
| 138 | 4.2 | 7.7 | 0.6 | 8.3 |
| 165 | 4.2 | 7.8 | 0.9 | 8.7 |
| 201 | 3.2 | 7.1 | 0.5 | 7.6 |

(Cellco 11, Q. 18, map; Cellco 10, Q. 9, map)

- Placing Cellco antennas on the proposed alternate one site tower at a point 150 feet AGL would provide the following within a four mile radius of the proposed prime site.

Proposed Alternate One Site Tower

| Route | ( -75 dbm | ( -90 dbm | Gap < -90 dbm | Total Miles |
| --- | --- | --- | --- | --- |
| 49 | 3.2 | 8.1 | 0.2 | 8.3 |
| 138 | 2.6 | 7.5 | 0.8 | 8.3 |
| 165 | 5.1 | 7.8 | 0.9 | 8.7 |
| 201 | 2.8 | 6.6 | 1.0 | 7.6 |

(Cellco 10, Q. 9, map; Cellco 11, Q. 18, map)

- Placing Cellco antennas on the proposed alternate two site tower at a point 197 feet AGL would provide the following coverage within a four mile radius of the proposed prime site.

Proposed Alternate Two Site Tower

| Route | ( -75 dbm | ( -90 dbm | Gap < -90 dbm | Total Miles |
| --- | --- | --- | --- | --- |
| 49 | 1.0 | 7.6 | 0.7 | 8.3 |
| 138 | 3.7 | 7.6 | 0.7 | 8.3 |
| 165 | 4.7 | 7.7 | 1.0 | 8.7 |
| 201 | 4.3 | 7.3 | 0.3 | 7.6 |

(Cellco 10, Q. 9, map; Cellco 11, Q. 18, map)

- Combining Cellco antennas placed on both the Wireless Solutions tower at a point 195-feet AGL and on the Sprint PCS tower at a point 150 feet AGL would provide the following coverage within a four mile radius of the proposed prime site.

Combined Wireless Solutions and Sprint PCS Towers

| Route | ( -75 dbm | ( -90 dbm | Gap < -90 dbm | Total Miles |
| --- | --- | --- | --- | --- |
| 49 | 1.6 | 7.5 | 0.8 | 8.3 |
| 138 | 2.3 | 7.5 | 0.8 | 8.3 |
| 165 | 2.4 | 7.2 | 1.5 | 8.7 |
| 201 | 2.4 | 6.8 | 0.8 | 7.6 |

(Cellco 11, Q. 18, map; Cellco 10, Q. 1, maps)

- Combining Cellco antennas placed on the proposed prime site tower at a point 150 feet AGL with antennas placed on the Wireless Solutions tower at a point 195 feet AGL with antennas placed on the Sprint PCS tower at a point 150 feet AGL would provide the following gaps within a four mile radius of the proposed prime site.

Combined Proposed Prime, Wireless Solutions and Sprint Towers

| Route | ( -75 dbm | ( -90 dbm | Gap < -90 dbm | Total Miles |
| --- | --- | --- | --- | --- |
| 49 | 4.3 | 8.3 | 0.0 | 8.3 |
| 138 | 4.2 | 7.9 | 0.4 | 8.3 |
| 165 | 4.2 | 7.9 | 0.8 | 8.7 |
| 201 | 3.2 | 7.4 | 0.2 | 7.6 |

(Cellco 11, Q. 18, map; Cellco 10, Q. 1, maps)

- Combining Cellco antennas placed on the proposed alternate one site tower at a point 150 feet AGL with antennas placed on the Wireless Solutions tower at a point 195 feet AGL with antennas placed on the Sprint PCS tower at a point 150 feet AGL would provide the following gaps within a four mile radius of the proposed prime site.

Combined Proposed Alternate One, Wireless Solutions and Sprint Towers

| Route | ( -75 dbm | ( -90 dbm | Gap < -90 dbm | Total Miles |
| --- | --- | --- | --- | --- |
| 49 | 3.2 | 8.1 | 0.2 | 8.3 |
| 138 | 2.6 | 7.5 | 0.8 | 8.3 |
| 165 | 5.1 | 7.9 | 0.8 | 8.7 |
| 201 | 2.8 | 7.1 | 0.5 | 7.6 |

(Cellco 11, Q. 18, map; Cellco 10, Q. 1, maps)

- Combining Cellco antennas placed on the proposed alternate two site tower at a point 197 feet AGL with antennas placed on the Wireless Solutions tower at a point 195 feet AGL with antennas placed on the Sprint PCS tower at a point 150 feet AGL would provide the following coverage within a four mile radius of the proposed prime site.

Combine Proposed Alternate Two, Wireless Solutions and Sprint Towers

| Route | ( -75 dbm | ( -90 dbm | Gap < -90 dbm | Total Miles |
| --- | --- | --- | --- | --- |
| 49 | 1.8 | 8.2 | 0.1 | 8.3 |
| 138 | 4.0 | 7.7 | 0.6 | 8.3 |
| 165 | 4.7 | 8.0 | 0.7 | 8.7 |
| 201 | 4.8 | 7.5 | 0.1 | 7.6 |

(Cellco 11, Q. 18, map; Cellco 10, Q. 1, maps)