| DOCKET NO. 214 - Sprint Spectrum, L.P. d/b/a Sprint PCS application for a Certificate of Environmental Compatibility and Public Need for the construction, maintenance, and operation of a cellular telecommunications facility at 31F Clarks Falls Road or 472 Pendleton Hill Road, North Stonington, Connecticut. | } } } | Connecticut Siting Council April 3, 2002 |
| --- | --- | --- |

Findings of Fact

Introduction

- Sprint Spectrum L.P., d/b/a Sprint PCS (Sprint) in accordance with provisions of General Statutes §§ 16-50g through 16-50aa applied to the Connecticut Siting Council (Council) on October 9, 2001, for the construction, operation, and maintenance of a wireless telecommunications facility in North Stonington, Connecticut. (Sprint 1, p. 1)

- Sprint is a wholly-owned subsidiary of WirelessCo L.P. licensed by the Federal Communications Commission (FCC) to provide wireless personal communication service (PCS).  Sprint operates in 32 major trading areas within the United States including Connecticut. (Sprint 1, pp. 1-2)

- The party in this proceeding is the applicant.  (Transcript 1 3:00 p.m. (Tr. 1), p. 4)

- Pursuant to General Statutes § 16-50m, the Council, after giving due notice thereof, held a public hearing on December 19, 2001, beginning at 3:00 p.m. and continuing at 7:00 p.m. in the North Stonington Town Hall, 40 Main Street, North Stonington, Connecticut.  (Tr. 1, p. 2)

- The Council and its staff made inspections of the proposed prime and alternate sites on December 19, 2001.  During the field inspection, the applicant flew a balloon at the proposed prime and alternate sites to simulate the heights of the towers proposed at these locations.  (Tr. 1, p. 24)

- Pursuant to CGS § 16-50l(e), Sprint provided technical materials to the First Selectman for the Town of North Stonington.  On June 28, 2001 Sprint met with the First Selectman to discuss plans and proposed locations for telecommunications facilities in the Town of North Stonington.  The Town held a public informational meeting on July 24, 2001.  (Sprint 1, pp. 19-20)

PCS Service Design

- Sprint operates a digital personal communications service network using a 1900-megahertz (MHz) frequency signal allocated by the FCC.  This high frequency signal is twice that of traditional cellular service in the 800 MHz range and degrades quickly in areas of hilly terrain and dense foliage.  The size of the search area is limited in North Stonington by the hilly terrain in the area.  (Sprint 1, p. 10, p. 20, Tab 14; Tr. 1, pp. 17-18)

- Adjacent Sprint facilities that would hand off traffic with the proposed facility are as follows:

| Location | Distance and Direction from Rt. 49/216 intersection | Antenna at AGL (ft) |
| --- | --- | --- |
| Pierce Road, Preston | 8 miles/northwest | 150 |
| Preston Town Hall, Preston | 8 miles/northwest | 150 |
| Wintechog Hill Rd., No. Stonington | 4.6 miles/west | 248 |
| Fire Station, No. Stonington | 2.5 miles/southwest | 120 |
| Gillever Road, Griswold | 5.8 miles/north | 165 |
| Bumpin Hill, Stonington | 3.2 miles/south | 195 |
| Boombridge Rd., No. Stonington | 2.3 miles/southeast | 157.5 |
| Off I-95, Hopkinton, Rhode Island | 3.4 miles/east | 187 |

(Sprint 2, PHQ. 8)

- Use of alternative technologies like microcells or repeaters would be useful for filling coverage in small areas or providing service in buildings, but are limited as to coverage and capacity. Sprint identified the minimum signal level threshold for an area in North Stonington to be -94 dbm.  Presently, approximately a 3.5-mile gap in coverage exists along Route 49. (Sprint 1, p. 20; Tr. 1, p. 20; Sprint 1, Tab 14)

Site Search

- The Sprint search area is a polygon with its center located approximately 1300 feet east of Route 49 in North Stonington. No structures are located within or near this search area. (Sprint 1, Tab 16; Tr. 1, pp. 18-19; Sprint 1, Tab 14, p. 5)

- Sprint identified and investigated six potential sites in North Stonington, including the proposed and alternate sites.  Four of the potential sites were rejected.  A site at 629 Wyassup Road was rejected due to an inability to reach a lease agreement with the owner; a site at 108 Fowler Road was rejected due to its location too far to the north and a coverage gap on Route 49; a site at 115 Fowler Road was too far to the north, had an unacceptable coverage gap on Route 49 and the property owners were not interested in negotiating a lease; and a site on Pendleton Hill Road was rejected due to its location too far to the north and a coverage gap.  (Sprint 1, p. 22)

Need and Coverage

- In 1996, the United States Congress recognized a nationwide need for high quality wireless telecommunications services, including cellular telephone service.  The Federal Telecommunications Act of 1996 seeks to promote competition, encourage technical innovations, and foster lower prices for telecommunications services. Furthermore, the Federal government has preempted the determination of public need for wireless service by the states, and has established design standards to ensure technical integrity and nationwide compatibility among all systems. (Telecommunications Act of 1996, Definition of Act, Sections 256, and 704)

- Coverage from surrounding existing facilities located (see Finding of Fact # 8) on roads within a three-mile radius of the intersection of Route 49 and Route 216 indicates the following coverage gaps.  Gaps are defined as areas receiving less than -94 dbm coverage. The primary purpose of this application is to provide coverage to these gaps in coverage and provide hand-off capability to adjacent sites.

Existing Coverage

(See Appendix A)

| Route | Gaps (approximate miles) < -94 dbm | Total Road Miles |
| --- | --- | --- |
| 49 | 3.5 | 6.00 |
| 216 | 1.0 | 2.40 |
|  | 4.5 | 8.40 |

(Sprint 1, Tab 9; Sprint 2, PHQ. 8, coverage models; Tr. 1, pp. 19-20)

- Existing coverage combined with Sprint antennas on the proposed prime or alternate site tower at 150 feet AGL would leave coverage gaps of approximately 0.3 miles within a three mile radius of the intersection of Route 49 and Route 216 as follows:

Proposed Prime/Alternate Site Tower at a height of 150 feet AGL

(See Appendix B)

| Route | Gaps (miles) < -94 dbm | Total Road Miles |
| --- | --- | --- |
| 49 | 0.3 | 6.00 |
| 216 | 0.0 | 2.40 |
|  | 0.3 | 8.40 |

(Sprint 2, PHQ. 8, coverage models)

- Existing coverage combined with Sprint antennas on the proposed prime or alternate site tower at 120 feet AGL would leave coverage gaps of approximately 0.6 miles within a three-mile radius of the intersection of Route 49 and 216 in Connecticut as follows:

Proposed Prime/Alternate Site Tower at a height of 120 feet AGL

(See Appendix C)

| Route | Gaps (miles) < -94 dbm | Total Road Miles |
| --- | --- | --- |
| 49 | 0.3 | 6.00 |
| 216 | 0.3 | 2.40 |
|  | 0.6 | 8.40 |

(Sprint 2, PHQ. 8, coverage models)

Proposed Prime

- The proposed prime site would be located on an approximately 62-acre parcel at 31F Clarks Falls Road, owned by Donald and Barbara Jones, in North Stonington, Connecticut.  The proposed site is within a birch-oak-maple forest, and no homes are visible from the proposed site.  An understory of mountain laurel and blueberry is within and around the proposed site.  (Sprint 1, p. 1, p. 4; Department of Environmental Protection (DEP) Comments of 12/17/01)

- The topography surrounding the proposed site is characterized by rolling hills, ranging from approximately 60 feet above mean sea level (AMSL) to 400 feet AMSL.  The proposed site has an elevation of 234 feet AMSL.  (Sprint 1, Tab 11, p. 1)

- There are two structures within a 1000-foot radius of the proposed site on an abutting property owned by Ray and Sherri Jones.  The nearest of the two structures stands approximately 800 feet southeast of the proposed site.  (Sprint 2, PHQ. 1, Ex. A)

- Access to the proposed prime site would be from Clarks Falls Road via an existing 10-foot wide dirt road approximately 4800 feet in length.  The access road turns to pavement for a distance of approximately 220 feet, the pavement then ends, and from this point Sprint would construct a 12-foot wide 280-foot gravel access road to the tower compound.  An existing two-foot high stone wall crosses the route of the proposed access drive.  A 30-foot section of the wall would have to be removed to construct the access road.  (Sprint 1, p. 9)

- The proposed site is zoned R-80 rural preservation district.  The site is currently used for limited logging by the property owners.  (Sprint 1, p. 16)

- Utilities would be brought into the proposed site underground from Clarks Falls Road.  (Sprint 1, p. 9)

- The proposed site would consist of a 100-foot by 100-foot leased area.  Sprint would enclose a 50-foot by 50-foot tower compound surrounded by a 7-foot high security fence containing an eight-foot six-inch by twenty-foot concrete equipment pad.  (Sprint 1, p.4, Tab 7, site plan)

Proposed Alternate Site

- The proposed alternate site would be located on an approximately eight-acre parcel at 472 Pendleton Hill Road (Route 49) in North Stonington, Connecticut, owned by Sally Hounslea. The alternate site is within a reverting field of sumac, pin cherry and red cedar.  The lessor's home and one home to the south at 464 Pendleton Hill Road are visible from the site.  (Sprint 1, p. 1, p. 4; DEP Comments of 12/17/01)

- The topography surrounding the alternate site is characterized by rolling hills ranging in elevation from 60 feet AMSL to 400 feet AMSL.  The proposed alternate site has an elevation of 216 feet AMSL and is approximately 0.25 miles west of the proposed site.  (Sprint 1, Tab 12, p. 1; Tab 5, map)

- There are 11 structures within a 1000-foot radius of the alternate site.  The nearest structure stands on an adjacent property owned by David and Gayle Phoenix approximately 375 feet to the southwest.  (Sprint 2, PHQ. 1, Ex. B; Sprint 1, Tab 7, map)

- Access to the alternate site would be from Pendleton Hill Road via a new 610-foot long 12-foot wide gravel access road.  (Sprint 1, p. 9)

- The alternate site is zoned R-80 rural preservation district.  (Sprint 1, p. 16)

- Utilities would be brought into the alternate site from Pendleton Hill Road overhead to a proposed utility pole at the beginning of the proposed access road, and from the new utility pole the utilities would follow the access road underground to the tower compound.  (Sprint 1, p. 9)

- The alternate site would consist of a 100-foot by 100-foot leased area.  Sprint would enclose a 50-foot by 50-foot tower compound surrounded by a 7-foot high security fence containing an eight-foot six-inch by twenty-foot concrete equipment pad.  (Sprint 1, p. 4, Tab 8, site plan map)

Tower Design

- Sprint would construct a 150-foot monopole at either proposed site with 12 antennas mounted on a triangular platform with four antennas per sector, designed in accordance with Electronic Industries Association (EIA) Standard 222-Revision F, of Structural Standards for Steel Antenna Towers and Antenna Support Structures.  A global positioning system (GPS) antenna would be mounted at 80 feet AGL.  (Sprint 1, p. 4, p. 8, Tab 7, Lease Area Plan)

- One carrier other than Sprint, AT&T, had expressed an interest in using the proposed tower, but AT&T has since declined use of the proposed tower.  (Tr.1, p. 16)

- Sprint would design the monopole and its foundation to support two additional carriers.  (Sprint 1, p. 7)

- Sprint would allow without charge any local authority or emergency response system to use the proposed tower, as long as it is consistent with the monopole's structural integrity.  The Town of North Stonington has not indicated an interest in using this tower.  (Sprint 1, p. 6; Tr. 1, p. 34)

- To maintain operations during power outages, the proposed sites would include a battery back-up system, but no generator or fuel tank on site.  If a power outage exceeded 24 hours in duration, a gasoline-powered electrical generator would be brought to the proposed site.  (Sprint 1, p. 8, p. 13; Tr. 1, p. 35)

Costs

- The approximate costs of construction to Sprint for both the proposed or alternate site are estimated as follows:

| Site work Concrete Work Monopole and antenna installation Electrical/telecommunications Service and grounding system Radio equipment Total Construction Budget Estimate | $68,000 41,500 40,000 50,000 103,000 $302,500 |
| --- | --- |

(Sprint 1, Tab 19; Tr. 1, p. 14)

Environmental Considerations

- There are no threatened or endangered species occurring in the vicinity of the proposed or alternate sites, based on a review of the Connecticut Department of Environmental Protection Natural Diversity Database.  (Sprint 1, Tab 21, Tab 22)

- No wetlands were identified within the proposed lease area, the access easement, or within 100 feet of the proposed construction activities at the proposed or alternate sites.  (Sprint 1, p. 13, Tab 21, Tab 22)

- The State Historic Preservation Office (SHPO) has determined that the proposed towers at the prime or alternate site would have no effect on the State's archaeological heritage.  However, the SHPO has stated that all construction-related activities at the alternate site must avoid physical alteration of the fieldstone foundation and granite steps located approximately 35 feet north of the route of the proposed access road.  (Sprint 1, Tab 21, Tab 22, SHPO letter of April 19, 2001)

- No trees of more than twelve inches in diameter would be removed during construction of the proposed prime site access drive or tower compound.  Two trees would be removed during construction of the access drive leading to the alternate site.  (Sprint 1, pp. 15-16)

- Sprint would install erosion and sediment controls prior to commencement of construction in accordance with the Connecticut Guidelines for Soil Erosion and Sediment Control.  (Sprint 1, p. 12)

- Neither the proposed prime or alternate tower would require marking or lighting pursuant to Federal Aviation (FAA) criteria.  (Sprint 2, PHQ. 6)

- The electromagnetic radio frequency power density calculation using the FCC Office of Engineering and Technology Bulletin 65, August 1997, using conservative worst-case approximation of radio frequency power density levels at the base of the proposed tower with all Sprint antennas transmitting simultaneously on all channels at full power would be 7.6 percent of the American National Standards Institute (ANSI) standard for a 150-foot tower at both the proposed prime and alternate sites.  (Sprint 1, pp. 22-23; Tab 18)

- The tower radius of both the proposed prime and alternate tower would not extend beyond the respective property boundaries.  No structures other than telecommunications equipment would be within the tower radius.  (Sprint 1C and 1D)

Visibility

- The visibility analysis within a two-mile radius of the proposed prime site assumes that the trees are of a uniform height of 75 feet and the forest cover represents approximately 6313 acres or 79 percent of the 8042-acre study area.  The 150-foot monopole tower would be visible from approximately 120-acres or 1.5 percent of the study area.  Sprint conducted a balloon test at various locations with the following results:

Visibility of the Proposed 150-foot Prime tower

| Location | Visible | Distance and Direction to Tower Site |
| --- | --- | --- |
| Clarks Falls Road | Yes | 0.89 miles to northwest |
| Clarks Falls Road | Yes | 1.26 miles to northwest |
| Denison Hill Road | Yes | 0.79 miles to northwest |
| Chester Main Road | Yes | 0.61 miles to northwest |
| Denison Hill Road | Not visible | 1.08 miles to southwest |
| Pendleton Hill Road | Not visible | 0.38 miles to southeast |
| Pendleton Hill Road | Not visible | 0.66 miles to northeast |
| Boombridge Road | Not visible | 0.69 miles to northwest |
| Clarks Falls Road | Not visible | 1.47 miles to northwest |

(Sprint 1, Tab 11)

- The visibility analysis within a two-mile radius of the proposed alternate site assumes that the trees are of a uniform height of 75 feet and the forest cover represents 6364 acres or 79 percent of the 8042-acre study area.  Sprint conducted a balloon test at various locations with the following results:

Visibility of Proposed 150-foot Alternate Tower

| Location | Visible | Distance and Direction to Tower Site |
| --- | --- | --- |
| Pendleton Hill Road | Yes | 0.11 miles to southeast |
| Pendleton Hill Road | Yes | 0.15 miles to southeast |
| Chester Main Road | Yes | 1.44 miles to northeast |
| Hangman Hill Road | Yes | 1.29 miles to northeast |
| Pendleton Hill Road | Yes | 0.18 miles to northeast |
| Pendleton Hill Road | Yes | 0.80 miles to northeast |
| Pendleton Hill Road | No | 0.40 miles to southeast |
| Pendleton Hill Road | No | 0.43 miles to northeast |
| Hangman Hill Road | No | 1.52 miles to northeast |
| Hangman Hill Road | No | 1.38 miles to southeast |
| Grindstone Hill Road | No | 0.71 miles to southeast |
| Puttker Road | No | 1.00 mile to southwest |
| Denison Hill Road | No | 0.86 miles to northeast |

Route 49 is designated as a state scenic road.  The alternate site tower would be prominently visible from the home at 464 Pendleton Hill Road (Route 49) south of the alternate site.  (Sprint 1, Tab 12; DEP Comments of 12/17/01, p. 2; Tr. 2, p. 27)

APPENDIX A

Existing Sprint Coverage

APPENDIX B

Proposed/Alternate Towers at 150 feet

APPENDIX C

Proposed Prime/Alternate Towers at 120 feet