| DOCKET NO. 321 – Optasite, Inc. and Omnipoint Communications, Inc. application for a Certificate of Environmental Compatibility and Public Need for the construction, maintenance and operation of a telecommunications facility at 940 Meriden Road in Waterbury, Connecticut. | } } } | Connecticut Siting Council February 27, 2007 |
| --- | --- | --- |

Opinion

On September 14, 2006, Optasite, Inc. (Optasite) and Omnipoint Communications, Inc. (T-Mobile) applied to the Connecticut Siting Council (Council) for the issuance of a Certificate of Environmental Compatibility and Public Need (Certificate) for the construction, maintenance and operation of a wireless telecommunications facility at 940 Meriden Road in Waterbury, Connecticut. The applicant sought to develop a facility on the 104-acre Pine Grove Cemetery located in the eastern part of Waterbury. This location would enable T-Mobile to provide wireless service along I-84 and Meriden Road. Sprint/Nextel Corporation (Nextel) was an intervenor in this proceeding and would install antennas on this site to provide capacity relief for overloaded facilities in the vicinity.

At the proposed location, Optasite would erect a 110-foot steel monopole tower. The tower would be located within a 60-foot by 60-foot compound that would include a 12-foot by 20-foot equipment shelter for Sprint/Nextel. The compound would be enclosed by an eight-foot high chain link fence. The tower would be designed to accommodate the antennas of up to four carriers. Vehicular access to the facility would extend over existing driveways and then over a new 250-foot gravel driveway that would be designed to avoid crossing a buried septic system pipe. Utility services would extend underground along the gravel drive.

The tower’s setback radius would be completely contained within the cemetery property.

The proposed tower would be visible year-round from approximately 33 acres. It would be seasonally visible from approximately 91 acres. Approximately eight residences would have partial year-round views of the tower; 36 residences would have partial seasonal views of the tower.  Visibility of the tower is limited in part by the number of mature, deciduous trees in the area where the tower would be erected.

The closest wetlands to the site are over 300 feet away. No trees with a diameter of six inches or greater at breast height would be cleared to make way for the facility.

No endangered or threatened species are known to inhabit the area of the site.

The proposed project would have no effect on historic, architectural, or archaeological resources listed on or eligible for the National Register of Historic Places.

According to a methodology prescribed by the FCC Office of Engineering and Technology Bulletin No. 65E, Edition 97-01 (August 1997), the combined radio frequency power density levels of the T-Mobile’s and Nextel’s antennas proposed to be installed on the tower have been calculated to amount to 15.457% of the FCC’s Maximum Permissible Exposure, as measured at the base of the tower. This percentage is well below federal and state standards established for the frequencies used by wireless companies.  If federal or state standards change, the Council will require that the tower be brought into compliance with such standards.  The Council will require that the power densities be recalculated in the event other carriers add antennas to the tower. The Telecommunications Act of 1996 prohibits any state or local agency from regulating telecommunications towers on the basis of the environmental effects of radio frequency emissions to the extent that such towers and equipment comply with FCC’s regulations concerning such emissions.

Both T-Mobile and Nextel provided sufficient data to support the need for a tower at this location. T-Mobile’s antennas at this site would provide added coverage and offloading of adjacent sites that primarily serve the heavily traveled Interstate Highway I-84. Nextel plans to use the tower to resolve interference and capacity issues it is currently experiencing in this area.

Based on the record in this proceeding, the Council finds that the effects associated with the construction, operation, and maintenance of the proposed telecommunications facility, including effects on the natural environment; ecological integrity and balance; public health and safety; scenic, historic, and recreational values; forests and parks; air and water purity; and fish and wildlife are not disproportionate either alone or cumulatively with other effects when compared to need, are not in conflict with policies of the State concerning such effects, and are not sufficient reason to deny this application.  Therefore, the Council will issue a Certificate for the construction, operation, and maintenance of a telecommunications facility, which would include a 110-foot steel monopole tower, at the proposed site at 940 Meriden Road in Waterbury, Connecticut.