| DOCKET NO. 344 - MCF Communications bg, Inc. and Omnipoint Communications, Inc. application for a Certificate of Environmental Compatibility and Public Need for the construction, maintenance and operation of a telecommunications facility located at Rich Road, Thompson, Connecticut. | } } } | Connecticut Siting Council January 10, 2008 |
| --- | --- | --- |

# Opinion

On July 27, 2007, MCF Communications bg, Inc. (MCF) and Omnipoint Communications, Inc. (T-Mobile) applied to the Connecticut Siting Council (Council) for the issuance of a Certificate of Environmental Compatibility and Public Need (Certificate) for the construction, maintenance and operation of a wireless telecommunications facility on Rich Road in Thompson, Connecticut. The applicants seek to develop a facility on an 8-acre parcel owned by the Town of Thompson. This property was vacant at the time of application. The proposed facility would provide coverage along Interstate I-395 and adjacent areas in the Town of Thompson.

At this location, MCF would lease a 100-foot by 100-foot parcel within which it would erect a 150-foot steel monopole tower within a 50-foot by 90-foot fenced compound. The tower would be designed to accommodate three additional wireless carriers and public safety antennas of the Town of Thompson. Vehicular access would be via a 132-foot gravel drive that would be extended from Rich Road. Utilities would be extended underground from Rich Road and would follow the access drive to the facility. No landscaping is proposed for the facility because the area in which the facility would be located is well vegetated and would be screened from Rich Road

The proposed tower’s setback radius would be contained within the town property.

The proposed tower would be visible year-round from approximately 392 acres within a two-mile radius of the site. It would be seasonally visible from an additional 32 acres. Approximately 96 residences would have partial year-round views of the tower; 19 additional residences would have seasonal views of the tower.

The nearest wetland is approximately 194 feet west of the proposed facility. Twenty-two trees with a diameter at breast height of six inches or more would be cleared to develop the proposed facility.

No known populations of species listed as endangered, threatened or of special concern occur at the site of the proposed facility.

The Narragansett Indian Tribal Historic Preservation Office found no evidence of cultural resources of significance to the Narragansett Tribe at the proposed site. Moreover, the proposed facility would have no effect upon Connecticut’s archaeological heritage.

According to a methodology prescribed by the FCC Office of Engineering and Technology Bulletin No. 65E, Edition 97-01 (August 1997), the combined radio frequency power density levels of the antennas proposed to be installed on the tower have been calculated to amount to 10.5% of the FCC’s Maximum Permissible Exposure, as measured at the base of the tower. This percentage is well below federal and state standards established for the frequencies used by wireless companies.  If federal or state standards change, the Council will require that the tower be brought into compliance with such standards.  The Council will require that the power densities be recalculated in the event other carriers add antennas to the tower. The Telecommunications Act of 1996 prohibits any state or local agency from regulating telecommunications towers on the basis of the environmental effects of radio frequency emissions to the extent that such towers and equipment comply with FCC’s regulations concerning such emissions.

The Council finds that the proposed facility would provide commercial wireless coverage in an area where there is a need for such coverage and that it would provide an opportunity for the Town of Thompson to improve the coverage of its emergency services wireless communications network.

Based on the record in this proceeding, the Council finds that the effects associated with the construction, operation, and maintenance of the proposed telecommunications facility, including effects on the natural environment; ecological integrity and balance; public health and safety; scenic, historic, and recreational values; forests and parks; air and water purity; and fish and wildlife are not disproportionate either alone or cumulatively with other effects when compared to need, are not in conflict with policies of the State concerning such effects, and are not sufficient reason to deny this application.  Therefore, the Council will issue a Certificate for the construction, operation, and maintenance of a telecommunications facility, which would include a 150-foot monopole tower, at the proposed site on Rich Road in Thompson, Connecticut.